## Slide 1: AVR Assembly Language Programming Chapter 2 (pp 75 - 79)
The AVR microcontroller
and embedded
systems
using assembly and c

## Slide 2: The AVR Assembler
We use the AVRASM2 assembler that comes with AVR studio
The Assembler performs the conversion from English mnemonics to opcodes that are programmed into the microcontroller
C compilers generate assembly language mnemonics that are then assembled by an assembler
Much confusion arises when one does not have a conceptual understanding of the different assembly phases

## Slide 5: Assembler Directives

## Slide 6: Assembler Directives

## Slide 22: Assembler Directives .EQU and .SET
.EQU name = value
  Example:
.EQU COUNT = 0x25
  LDI R21, COUNT ;R21 = 0x25
  LDI R22, COUNT + 3 ;R22 = 0x28
.SET name = value
  Example:
  .SET COUNT = 0x25
  LDI R21, COUNT ;R21 = 0x25
  LDI R22, COUNT + 3 ;R22 = 0x28
  .SET COUNT = 0x19
  LDI R21, COUNT ;R21 = 0x19

## Slide 23: Assembler Directives .INCLUDE
.INCLUDE "filename.ext"
.equ SREG = 0x3f
.equ SPL = 0x3d
.equ SPH = 0x3e
....
.equ INT_VECTORS_SIZE = 42 ; size in words
M32def.inc
.INCLUDE "M32DEF.INC"
LDI R20, 10
OUT SPL, R20
Program.asm

## Slide 24: Assembler Directives .ORG
.ORG address
.ORG 0
LDI R16, 0x25
.ORG 0x7
LDI R17, 0x34
LDI R18, 0x31
Program.asm
00 E205
01 0000
02 0000
03 0000
04 0000
05 0000
06 0000
07 E314
08 E321
09 0000
0A 0000
assembler

## Slide 25: Assembler Functions

## Slide 26: Assembler Functions

## Slide 27: Assembler Operators

## Slide 28: Some Assembler Operators

## Slide 29: Some Assembler Operators

## Slide 30: Some Assembler Operators

## Slide 31: Some Assembler Operators

## Slide 32: Some Assembler Operators

## Slide 33: Some Assembler Operators

## Slide 34: Some Assembler Operators

## Slide 35: Some Assembler Operators

## Slide 36: Assembler Preprocessor

## Slide 37: Assembler
Assembly
Machine
Language
assembler

## Slide 38: Flash memory and PC register
16-bit
00 E205
01 E314
02 E321
03 0F01
04 0F02
05 E01B
06 0F01
07 9300
08 0300
09 940C
0A 0009
E205
E314
E321
0F01
0F02
E01B
0F01
9300
0300
940C
0009
0
1
2
3
4
5
6
7
8
9
A
B
LDI R16, 0x25
LDI R17, $34
LDI R18, 0x31
ADD R16, R17
ADD R16, R18
LDI R17, 11
ADD R16, R17
STS SUM, R16
HERE:JMP HERE

## Slide 39: Fetch and execute
Old Architectures
16-bit
00 E205
01 E314
02 E321
03 0F01
04 0F02
05 E01B
06 0F01
07 9300
08 0300
09 940C
0A 0009
Fetch
Execute
Instruct 1
Instruct 2
Instruct 3
Instruct 4

## Slide 40: Pipelining
Pipelining
16-bit
00 E205
01 E314
02 E321
03 0F01
04 0F02
05 E01B
06 0F01
07 9300
08 0300
09 940C
0A 0009
Fetch
Execute
Instruct 1
Instruct 2
Instruct 3
Instruct 4

## Slide 41: How to speed up the CPU
Increase the clock frequency
  More frequency  More power consumption & more heat
  Limitations
Change the architecture
  Pipelining
  RISC

## Slide 42: Changing the architecture RISC vs. CISC
CISC (Complex Instruction Set Computer)
  Put as many instruction as you can into the CPU
RISC (Reduced Instruction Set Computer)
  Reduce the number of instructions, and use your facilities in a more proper way.

## Slide 43: RISC architecture
Feature 1
  RISC processors have a fixed instruction size. It makes the task of instruction decoder easier.
    In AVR the instructions are 2 or 4 bytes.
  In CISC processors instructions have different lengths
    E.g. in 8051
      CLR C ; a 1-byte instruction
      ADD A, #20H ; a 2-byte instruction
      LJMP HERE ; a 3-byte instruction

## Slide 44: RISC architecture
Feature 2: reduce the number of instructions
  Pros: Reduces the number of used transistors
  Cons:
    Can make the assembly programming more difficult
    Can lead to using more memory

## Slide 45: RISC architecture
Feature 3: limit the addressing mode
  Advantage
    hardwiring
  Disadvantage
    Can make the assembly programming more difficult

## Slide 46: RISC architecture
Feature 4: Load/Store
  LDS R20, 0x200
  LDS R21, 0x220
  ADD R20, R21
  STS 0x230, R20

## Slide 47: RISC architecture
Feature 5 (Harvard architecture): separate buses for opcodes and operands
  Advantage: opcodes and operands can go in and out of the CPU together.
  Disadvantage: leads to more cost in general purpose computers.
CPU
Address bus
Data
Memory
Data bus
Control bus
Address bus
Code
Memory
Data bus
Control bus
Fetch
Execute
LDS R20, 0x100
ADD R20, R21
LDS R20, 0x100 ; R20 = [0x100]
ADD R20,R21 ; R20 = R20 + R21

## Slide 48: RISC architecture
Feature 6: more than 95% of instructions are executed in 1 machine cycle

## Slide 49: RISC architecture
Feature 7
  RISC processors have at least 32 registers. Decreases the need for stack and memory usages.
    In AVR there are 32 general purpose registers (R0 to R31)

## Slide 50: Example 2-5
Write the program in AVR Studio to verify that The Z flag is the one when the result is zero. Verify:
Note: do not forget to add iat the beginning of the program:
.include "M32DEF.inc"

## Slide 51: Example 2- 6
Verify using AVR Studio

## Slide 52: Example 2- 7
Verify using AVR Studio

## Slide 53: Example 2- 8
Verify using AVR Studio

## Slide 54: Problems (5)

## Slide 55: Programming Exercise

## Slide 56: Problems (6)

## Slide 57: Problem (7)

## Slide 58: Problem (8)