## Slide 1: MOS Differential Amplifiers
Two matched transistors (Q1 and Q2) joined and biased by a constant current source I.
FET’s should not enter triode region of operation.
Fig.: MOS differential-pair configuration.
Figure: The basic MOS differential-pair configuration.

## Slide 2: Operation with a Common –Mode Input Voltage
Consider case when two gate terminals are joined together.
  Connected to a common-mode voltage (VCM).
  vG1 = vG2 = VCM
Q1 and Q2 are matched.
Current I will divide equally between the two transistors.
  ID1 = ID2 = I/2, VS = VCM – VGS
    where VGS is the gate-to-source voltage.

## Slide 3: Operation with a Common –Mode Input Voltage
Equations (8.2) through (8.8) describe this system, if channel-length modulation is neglected.
  Note specification of input common-mode range (VCM).
VCS: Voltage across the current souce
(Use VDS≥Vov)
(Use VCM≥VS+VGS)

## Slide 4: Operation with a Common –Mode Input Voltage
Symmetry circuit.
Common-mode voltage.
Current I divides equally between two transistors.
The difference between two drains is zero (vD2 – vD1)=0
The differential pair rejects the common-mode input signals

## Slide 5: Operation with a Differential Input Voltage
The MOS differential pair with a differential input signal vid applied.
With vid positive: vGS1 > vGS2, iD1 > iD2, and vD1 < vD2; thus (vD2 - vD1) will be positive.
With vid negative: vGS1 < vGS2, iD1 < iD2, and vD1 > vD2; thus (vD2 - vD1) will be negative.
The differential pair responds to a difference-mode or differential input signals.

## Slide 6: Operation with a Differential Input Voltage
Figure: The MOS differential pair with a differential input signal vid applied.
At this point, it is useful to inquire about the value of vid that causes the entire bias current I to flow in one of the two transistors. In the positive direction, this happens when vGS1 reaches the value that corresponds to iD1 = I, and vGS2 is reduced to a value equal to the threshold voltage Vt , at which point vS = –Vt . The value of vGS1 can be found from
(vGS1 – Vt = vid)

## Slide 7: Operation with a Differential Input Voltage
Differential input voltage.
Response to the differential input signal.
The current I can be steered from one MOS to the other by varying the differential input voltage in the range:
When differential input voltage is very small, the differential output voltage is proportional to it, and the gain is high.

## Slide 8: Small-Signal Operation of MOS Differential Pair
Linear amplifier
Differential gain
Common-mode gain
Common-mode rejection ratio(CMRR)
Mismatch on CMRR

## Slide 9: Differential Gain
a common-mode voltage applied to set the dc bias voltage at the gates.
vid applied in a complementary (or balanced) manner.

## Slide 10
Differential Gain
Two reasons single-ended amplifiers are preferable:
  Insensitive to interference.
  Do not need bypass coupling capacitors.

## Slide 11
Differential Gain
For MOS pair, each device operates with drain current I/2 and corresponding overdrive voltage (VOV).
  a 1
MOS: gm = I/VOV
BJT: gm = aI/2VT
MOS: ro = |VA|/(I/2).

## Slide 12: Differential Gain
Signal voltage at the joint source connection must be zero.

## Slide 13: Differential Gain
An alternative way of looking at the small-signal operation of the circuit.
ground
id
-id
Vs = 0

## Slide 14: Differential Gain
Differential gain
  Output taken single-ended
  Output taken differentially
  Advantages of output signal taken differentially
    Reject common-mode signal
    Increase in gain by a factor of 2(6dB)

## Slide 15: Differential Gain
MOS differential amplifier with ro and RSS taken into account.

## Slide 16: Differential Gain
Equivalent circuit for determining the differential gain.
Each of the two halves of the differential amplifier circuit is a common-source amplifier, known as its differential “half-circuit.”

## Slide 17: Differential Gain
Differential gain
  Output taken single-ended
  Output taken differentially

## Slide 18: Common-Mode Gain
The MOS differential amplifier with a common-mode input signal vicm.

## Slide 19: Common-Mode Gain
Equivalent circuit for determining the common-mode gain (with ro ignored).
Each half of the circuit is known as the “common-mode half-circuit.”

## Slide 20: Common-Mode Gain
Common-mode gain
  Output taken single-ended
  Output taken differentially
Total resistance in Drain circuit
Total resistance in Source circuit

## Slide 21: Common-Mode Rejection Ratio
Common-mode rejection ratio(CMRR)
  Output taken single-ended
  Output taken differentially
  This is true only when the circuit is perfectly matched.

## Slide 22: Biasing in Integrated Circuits
Strive to realize as many of the functions required as possible using MOS transistors only.
    Large even moderate value resistors are to be avoided
    Constant-current sources are readily available.
    Coupling and bypass capacitors are not available to be used, except for external use.
Design Philosophy of Integrated Circuits

## Slide 23: Biasing in Integrated Circuits
Low-voltage operation can help to reduce power dissipation but poses a host of challenges to the circuit design.
Bipolar integrated circuits still offer many exciting opportunities to the analog design engineer.
Design Philosophy of Integrated Circuits

## Slide 24: Biasing mechanism for ICs
  BJT Circuits
    The basic BJT current source
    Current-steering
  MOSFET Circuits
    The basic MOSFET current source
    MOS current-steering circuits

## Slide 25: Biasing mechanism for ICs(cont’d)
  Current-mirror circuits with improved performance
    A bipolar mirror with base-current compensation
    The wilson current mirror
    The current steering circuits
    The widlar current source

## Slide 26: The Basic BJT Current Mirror

## Slide 27: A Simple BJT Current Source.
Disadvantages: Decreasing Io, increasing R
(simplified if 2/β<<1)

## Slide 28: Current Steering

## Slide 29: Current-Mirror Circuits with Improved Performance
Two performance parameters need to be improved:
  The accuracy of the current transfer ratio of the mirror.
  The output resistance of the current source.

## Slide 30: Current Mirror with Base-Current Compensation
Original current source
Original current source with Base-current compensation

## Slide 31: The Wilson Bipolar Current Mirror
(read textbook)

## Slide 32: The Widlar Current Source
(From IREF and Io, determine RE)

## Slide 33: The advantages of Widlar Current Source
Example6.2 p518
Widlar circuit allows the generation of a small constant current using relatively small resistors( saving in chip area ).
Another important characteristic of the widlar current source is that its output resistance is high.

## Slide 34: The Basic MOSFET Current Source

## Slide 35: MOS Current-Steering Circuits

## Slide 36: The Wilson MOS Current Mirror

## Slide 37: The Differential Amplifier with Active Load
Replace resistance RD with a constant current source results in a much high voltage gain as well as saving in chip area.
Convert the output from differential to single-ended.

## Slide 38: The Bipolar Differential Pair with Active Load
Active-loaded bipolar differential pair.
Quiescent analysis:
if the circuit is perfectly matched, no output
Current flows through the output Terminal.

## Slide 39: Differential-to-Single-Ended Conversion
A simple but inefficient approach for differential to single-ended conversion.
Drawback:
Lose a factor of
2(or 6 dB)

## Slide 40: The Active-Loaded MOS Differential Pair
DC analysis: No output current

## Slide 41: The Active-Loaded MOS Differential Pair
The circuit with a differential input signal applied, neglecting the ro of all transistors.
AC analysis: output current is twice

## Slide 42: Multistage Amplifiers
The first stage (input stage) is differential-in, differential-out and consists of Q1 and Q2.
The second stage is differential-in, single-ended-out amplifier which consists of Q3 and Q4.
The third stage is CE amplifier which consists of pnp transistor Q7 to shifting the dc level.
The last stage is the emitter follower.
Biasing stage.

## Slide 44: Multistage Amplifier
Equivalent circuit for calculating the gain of the input stage of the example.
Input differential resistance
Gain of first stage

## Slide 45: Multistage Amplifier
Equivalent circuit for calculating the gain of the second stage of the example.
Gain of second stage

## Slide 46: Multistage Amplifier
Equivalent circuit for calculating the gain of the third stage of the example.
Gain of third stage

## Slide 47: Multistage Amplifier
Equivalent circuit for calculating the gain of the output stage of the example.
Gain of output stage
Output resistance

## Slide 48
Summary
The differential-pair or differential-amplifier configuration is most widely used building block in analog IC designs. The input stage of every op-amp is a differential amplifier.
There are two reasons for preferring differential to single-ended amplifiers: 1) differential amplifiers are insensitive to interference and 2) they do not need bypass and coupling capacitors.
For a MOS (bipolar) pair biased by a current source I, each device operates at a drain (collector, assuming a = 1) current of I/2 and a corresponding overdrive voltage VOV (no analog in bipolar). Each device has gm=1/VOV (aI/2VT for bipolar).

## Slide 49
Summary
With the two input terminals connected to a suitable dc voltage VCM, the bias current I of a perfectly symmetrical differential pair divides equally between the two transistors of the pair, resulting in zero voltage difference between the two drains (collectors). To steer the current completely to one side of the pair, a difference input voltage vid of at least 21/2VOV is needed.
Superimposing a differential input signal vid on the dc common-mode input voltage VCM such that vI1 = VCM + vid/2 and vI2 = VCM – vid/2 causes a virtual signal ground to appear on the common-source (common-emitter) connection.

## Slide 50
The analysis of a differential amplifier to determine differential gain, differential input resistance, frequency response of differential gain, and so on is facilitated by employing the differential half-circuit which is a common-source (common-emitter) transistor biased at I/2.
An input common-mode signal vicm gives rise to drain (collector) voltage signals that are ideally equal and given by –vicm(RD/2RSS)[-vicm(RC/2REE) for the bipolar pair], where RSS (REE) is the output resistance of the current source that supplies the bias current I.
While the input differential resistance Rid of the MOS pair is infinite, that for the bipolar pair is only 2rp but can be increased to 2(b+1)(re+Re) by including resistances Re in the two emitters. The latter action, however, lowers Ad.
Summary