## Slide 1: 9.2. Internal Capacitive Effects and the High-Frequency Model of the MOSFET and BJT
MOSFET has internal capacitance (this is apparent).
  The gate capacitive effect: The gate electrode forms a parallel plate capacitor with the channel.
  The source-body and drain-body depletion layer capacitances: These are the capacitances of the reverse-biased pn-junctions.
Previously, it was assumed that charges are acquired instantaneously - resulting in steady-state model.
  This assumption poses problem for frequency analysis.
While coupling & bypass capacitors cause the gain of transistor amplifiers to fall off at the low frequency end, the gain falloff at high frequencies is caused by the capacitive effects internal to the transistors.
Physical structure of NMOS transistor

## Slide 2: The Gate Capacitive Effect
The gate capacitive effect can be modeled by the three capacitances Cgs, Cgd, and Cgb. The values of these capacitances can be determined as follows:
Cox: oxide capacitance
C4 and C5 are Cov

## Slide 3: The Junction Capacitances
The depletion-layer capacitances of the two reverse-biased pn junctions formed between each of the source and the drain diffusions and the body
where Csb0 is the value of Csb at zero body-source bias, VSB is the magnitude of the reverse bias voltage, and V0 is the junction built-in voltage (0.6 V to 0.8 V).
where Cdb0 is the capacitance value at zero reverse-bias voltage, and VDB is the magnitude of
this reverse-bias voltage.

## Slide 4
Figure 9.6 (a) High-frequency, equivalent-circuit model for the MOSFET. (b) The equivalent circuit for the case in which the source is connected to the substrate (body). (continued)
The High-Frequency MOSFET Model Fig. 9.6(a) shows the small-signal model of the MOSFET, including the four capacitances Cgs, Cgd, Csb, and Cdb. This model can be used to predict the high-frequency response of MOSFET amplifiers. But quite complex
for manual analysis.
In Fig. 9.6(b) - the source is connected to the body. In this model, Cgd, although small, plays a significant role in determining the high-frequency response of amplifiers and thus must be kept in the model.

## Slide 5
Figure 9.6: (continued) (c) The equivalent-circuit model of (b) with Cdb neglected (to simplify analysis).

## Slide 6: The MOSFET Unity-Gain Frequency (fT)
A figure of merit for the high-frequency operation of the MOSFET as an amplifier is the unity-gain frequency, fT, also known as the transition frequency. This is defined as the frequency at which the short-circuit current-gain of the common-source configuration becomes unity.
Figure shows the MOSFET hybrid-π model with the source as the common terminal between the input and output ports.
To determine the short-circuit current gain, the input is fed with a current-source signal Ii and the output terminals are short-circuited. It can be seen that the current in the short circuit is given by
Io = gmVgs – sCgdVgs

## Slide 7
The MOSFET Unity-Gain Frequency (fT)
Cgd is small, at the frequencies of interest the second term in this equation can be neglected,
Note: for physical frequencies s = jω, it can be seen that the magnitude of the current gain becomes unity at the frequency ωT = gm ⁄ (Cgs + Cgd)
(fT = ωT / 2)

## Slide 8
Table 9.1 The MOSFET High-Frequency Model
Model
Model Parameters

## Slide 9: 9.2.2. The BJT
Like MOSFET, previously it was assumed that transistor action was instantaneous.
  steady-state model
  neglects frequency-dependence
Actual transistors exhibit charge-storage.
An augmented BJT model is required to examine this dependence.
The resulting augmented BJT model will be able to predict the observed dependence of amplifier gain on frequency, and the time delays that transistor switches and logic gates exhibit.

## Slide 10: 9.2.2. The BJT
The Base-Charging or Diffusion Capacitance Cde When the transistor is operating in the active mode, minority carrier charge is stored in the base region. For an npn transistor, the stored electron charge in the base, Qn
Which is the average time a charge carrier (electron) spends in crossing the base (10ps to 100ps)
Value of Cje at zero voltage
(The Collector-Base Junction capacitance)
Value of Cµ at zero voltage
CBJ Built in voltage (0.75V)
m
Grading coefficient of CBJ (0.3 to 0.5)
Notes: F is average time a charge carrier (electron) spends in crossing the base.

## Slide 11: 9.2.2. The BJT
Figure 9.8 The high-frequency hybrid-π model.
The High-Frequency Hybrid-π Model as seen in figure 9.8: there are two capacitances: the emitter–base capacitance Cπ = Cde + Cje and the collector–base capacitance Cμ . Typically, Cπ is in the range of a few picofarads to a few tens of picofarads, and Cμ is in the range of a fraction of a picofarad to a few picofarads.
Model resistance of silicon material of the base region
(Few tens of Ωs) Since rx <<< rπ , its effect is negligible at low frequencies , it becomes apparent in the high frequencies

## Slide 12: The Cutoff Frequency
The behavior of β (or hfe) versus frequency is normally given. To determine Cπ and Cμ , we shall derive an expression for hfe, the CE short-circuit current gain, as a function of frequency in terms of the hybrid-π components. For this purpose consider the circuit shown in Fig. 9.9, in which the collector is shorted to the emitter.
Figure 9.9 Circuit for deriving an expression for hfe(s) ≡ Ic ⁄ Ib

## Slide 13: The Cutoff Frequency
A node equation at C provides the short-circuit collector current Ic as
ωCμ << gm
where β0 is the low-frequency value of β. Thus hfe has a single-pole (or STC) response with a 3-dB frequency at ω = ωβ , where
ω
Current gain
βo
ωT
ωβ

## Slide 14
Figure 9.10 Bode plot for |hfe|
Figure 9.10 shows a Bode plot for |hfe|. From the –6-dB/octave slope, it follows that the frequency at which drops to unity, which is called the unity-gain bandwidth ωT,
The unity-gain bandwidth fT , also known as the transition frequency, is usually specified on the data sheets of a transistor.

## Slide 15
Note: the hybrid-π model of Fig. 9.8 characterizes transistor operation fairly accurately up to a frequency of about 0.2 fT .

## Slide 16: 9.3. High-Frequency Response of the CS and CE Amplifiers
Objective is to identify the mechanism that limits high-frequency performance of these important amplifier configurations. As well, we need to find a simple approach to estimate the frequency fH at which the gain falls by 3 dB below its value at midband frequencies, |AM|.
Figure 9.12: Frequency response of a direct-coupled (dc) amplifier. Observe that the gain does not fall off at low frequencies, and the midband gain AM extends down to zero frequency.

## Slide 17: 9.3.1. The Common-Source Amplifier
Figure 9.13(a) shows high-frequency equivalent-circuit model of a CS amplifier.
MOSFET is replaced with model of Figure 9.6(c).
It may be simplified using Thevenin’s theorem at the input side and by combining the three parallel resistances at the output side. The resulting simplified circuit is shown in Fig. 9.13(b).
Also, bridging capacitor (Cgd) may be redefined.
Cgd gives rise to much larger capacitance Ceq.
  The multiplication effect that it undergoes is known as the Miller Effect.
Figure 9.13 (a)

## Slide 18: 9.3.1. The Common-Source Amplifier
Figure 9.13: Determining the high-frequency response of the CS amplifier: (a) equivalent circuit; (b) the circuit of (a) simplified at the input and the output; (Continued)
Figure 9.13 (b)
Midband gain AM can be found from this
circuit by setting Cgs & Cgd to zero. The result is:

## Slide 19
Frequency response:
The common-source amplifier has one zero and two poles at higher frequencies
The amplifier gain falls off at frequencies beyond midband
The amplifier bandwidth is defined by the 3-dB frequency which is typically evaluated by the dominant pole (the lowest-frequency pole) in the transfer function
9.3.1. The Common-Source Amplifier

## Slide 20
Simplified analysis technique
  Assuming the gain is nearly constant ( -gmR’L)
  Find the equivalent capacitance of Cgd at the input (with identical Igd)
Replaced by Ceq
 Miller effect
Figure 9.13 (b)
9.3.1. The Common-Source Amplifier

## Slide 21
Neglect the small current Igd at the output
ωH is the upper 3-dB frequency
Thus: the high-frequency response will be that of a low-pass STC network with a
3-dB frequency fH determined by the time constant CinR′sig
Figure 9.13 (c)
9.3.1. The Common-Source Amplifier

## Slide 22: 9.3.1. The Common-Source Amplifier
Figure 9.13: (d) the frequency response plot, which is that of a low-pass, single-time-constant circuit.
Figure 9.13 (d)
Figure 9.13(d) shows a sketch of the magnitude of the high-frequency gain.

## Slide 23: Example 9.3

## Slide 24
Solution
where
Thus

## Slide 25: 9.3.2. The Common-Emitter Amplifier
Figure 9.14(a) shows high-frequency equivalent circuit of a CE amplifier.
  BJT is replaced.
  This figure applies to both discrete and IC amps.
This figure may be simplified using Thevenin’s theorem at the input side and by combining the three parallel resistances at the output side.
Cin is simply sum of Cπ and Miller capacitance Cμ(1+gmRL’)
Figure 9.14: Determining the high-frequency response of the CE amplifier: (a) equivalent circuit;
Figure 9.14 (a)

## Slide 26: 9.3.2. The Common-Emitter Amplifier
Figure 9.14: (b) the circuit of (a) simplified at both the input side and the output side; (continued)
Figure 9.14 (b)
The 3-dB frequency fH is given by
Where:

## Slide 27
Figure 9.14 (c) equivalent circuit with Cμ replaced at
the input side with the equivalent capacitance Ceq;
Figure 9.14 (d) sketch of the frequency-response plot, which is that of a low-pass STC circuit.

## Slide 28
Example 9.4
It is required to find the midband gain and the upper 3-dB frequency of the common-emitter amplifier of Fig. 9.4(a) for the following case: VCC = VEE = 10 V, I = 1 mA, RB = 100 kΩ, RC = 8 kΩ, Rsig = 5 kΩ, RL = 5 kΩ, β0 = 100, VA = 100 V, Cμ = 1 pF, fT = 800 MHz, and rx = 50 Ω.

## Slide 29
Solution
The transistor is biased at IC  1 mA. Thus the values of its hybrid-π model parameters are
The midband voltage gain is
Where RL′ = ro || RC || RL = (100 || 8 || 5) kΩ = 3 kΩ
 gmRL′ = 40 × 3 = 120 V/V
20log|AM| = 32 dB
To determine fH we first find Cin, Cin = Cπ + Cμ(1 + gmRL′) = 7 + 1(1 + 120) = 128 pF
and the effective source resistance R’sig

## Slide 30: 9.4.4. Miller’s Theorem
Figure 9.17(a)
Consider the situation shown in Figure 9.17(a).
  It is part of a larger circuit which is unknown.
Miller’s Theorem states that impedance Z can be replaced with two impedances:
  Z1 connected between node 1 and ground
    (9.76a) Z1 = Z/(1-K)
  Z2 connected between node 2 nd ground where
    (9.76b) Z2 = Z/(1-1/K)
Figure 9.17(b)

## Slide 31
Example 9.7
An ideal voltage amp. having a gain of -100 V/V with an impedance Z connected bw. its output and input terminals. Find the Miller equivalent circuit when Z is (a) a 1-M resistance, and (b) a 1-pF capacitance. In each case, use the equivalent circuit to determine Vo/Vsig.
Figure 9.18 Circuits for Example 9.7
Solution
(a) For Z = 1 MΩ, employing Miller’s theorem results in the equivalent circuit in Fig. 9.18(b), where
The voltage gain can be
(b) For Z as a 1-pF capacitance

## Slide 32
Solution
It follows that Z1 is a capacitance 101C = 101 pF and that Z2 is a capacitance 1.01C = 1.01 pF. The resulting equivalent circuit is shown in Figure below, from which the voltage gain can be found as follows:
This is the transfer function of a first-order low-pass network with a dc gain of −100 and a 3-dB frequency f3dB of
The multiplication of a feedback capacitance by (1−K) is referred to as Miller multiplication or Miller effect.

## Slide 33
9.5 A Closer Look at the High-Frequency
Response of the CS and CE Amplifiers
9.5.1 The equivalent circuit of a CS amplifier
• V ′sig & R′sig are the Thevenin equivalent of the signal generator.
• R′L represents the total resistance bw. output (drain) node and ground and includes
RD, ro, & RL.
Figure 9.19 Generalized high-frequency equivalent circuit for the CS amplifier

## Slide 34: 9.5.2. Analysis Using Miller’s Theorem
Figure 9.20: The high-frequency equivalent circuit model of the CS amplifier after the application of Miller’s theorem to replace the bridging capacitor Cgd by two capacitors: C1 = Cgd(1-K) and C2 = Cgd(1-1/K), where K = V0/Vgs.
Since Vo ≈ −gmVgsR′L, That is, K is given by K ≈ gmR′L
At the input side, the input capacitance Cin = Cgs +C1 together with R′sig forms an STC low-pass circuit with a pole freq. fPi:

## Slide 35: 9.5.2. Analysis Using Miller’s Theorem
At the output sides C′L = CL + C2 together with R′L forms an STC low-pass circuit with a pole freq. fPo,
Read the example 9.8 in the text book (page 734)

## Slide 36: Summary
The coupling and bypass capacitors utilized in discrete-circuit amplifiers cause the amplifier gain to fall off at low frequencies. The frequencies of the low-frequency poles can be estimated by considering each of these capacitors separately and determining the resistance seen by the capacitor. The highest-frequency pole is that which determines the lower 3-dB frequency (fL).
Both MOSFET and the BJT have internal capacitive effects that can be modeled by augmenting the device hybrid-pi model with capacitances.
  MOSFET: fT = gm/2p(Cgs+Cgd)
  BJT: fT = gm/2p(Cp+Cm)

## Slide 37: Summary
The internal capacitances of the MOSFET and the BJT cause the amplifier gain to fall off at high frequencies. An estimate of the amplifier bandwidth is provided by the frequency fH at which the gain drops 3dB below its value at midband (AM). A figure-of-merit for the amplifier is the gain-bandwidth product (GB = AMfH). Usually, it is possible to trade gain for increased bandwidth, with GB remaining nearly constant. For amplifiers with a dominant pole with frequency fH, the gain falls off at a uniform 6dB/octave rate, reaching 0dB at fT = GB.
The high-frequency response of the CS and CE amplifiers is limited by the Miller effect.