## Slide 1
Quiz 4.2
Deadline: April 17, 2020
a) Fig. 1 shows the Mosfet circuit with RD = RL = 10 kΩ, Rsig = 50 kΩ, RG = 3MΩ, Cgs = 5 pF, Cgd = 2 pF and gm = 2 mA/V. All capacitors CC1, CC2, and Cs are considered as short circuits.
Find unity-gain frequency of the transistor MOSFET (NOT the circuit).
Find Ceq using Miller effect.
Find the upper 3-dB frequency fH of the voltage gain vo/vsig.
Find the voltage gain AM = vo/vsig at middle frequency.
Estimate the voltage gain vo/vsig at 2fH. (Use concept of -6dB/octave or -20dB/decade)
Plot the Bode plot of A(jω) = vo/vsig and give sufficient information on the graph.
Fig. 1

## Slide 2
b) Fig. 2 shows the BJT circuit with RC = RL = 5 kΩ, Rsig = 2 kΩ, RB = 82kΩ, rx = 50Ω, Cπ = 20pF, Cμ = 5pF, Ic = 1mA and βo = 100. All capacitors CC1, CC2, and Cs are considered as short circuits
Find unity-gain frequency of the transistor BJT (NOT the circuit).
Find Ceq using Miller effect.
Find the upper 3-dB frequency fH.
Find the voltage gain AM = vo/vsig at middle frequency
Plot the Bode plot of A(jω) = vo/vsig and give sufficient information on the graph.
Fig. 2