## Slide 1
Quiz 6.1
Deadline: May 29, 2020
Question 1
The class B power amplifier is shown in the Figure. Given that two transistors are identical with VBE = VEB =0.7V, V+ = 20V, V- = -20V, RL = 8Ω and vI is a sinusoid varying from -16V to +16V.
What is the peak voltage vo?
Compute the power delivered to the load RL assuming that the waveform can be considered as the sinusoid.
Compute average power drawn from each supply .
Compute the efficiency of the amplifier.
What is the disadvantage of class B amplifier

## Slide 2
Question 2
The class AB power amplifier is shown in the Figure. Given that two transistors are complementary with iCn = iCp = 20mA corresponding to β = 50. Diodes D1 and D2 are identical with IS = 10-14 A and n = 1.
Find VBB If IBias = 10mA.
If RL = 8Ω and load power is 10W, Give your suggestion about the value of V+ and V-.