## Slide 1
Text book:
Sedra and Smith, “Microelectronic Circuits,” 6th Edition.
Lecture # 8: Signal generators and waveform-shaping circuits
International University
School of Electrical Engineering
ANALOG ELECTRONICS
Link: Blackboard to download materials

## Slide 2
Signal generators and waveform-shaping circuits
Introduction
17.1 Basic principles of sinusoidal oscillators
17.2 RC oscillator circuits
17.3 LC and crystal oscillators
17.4 Bistable Multivibrators
17.5 Generation of a standardized pulse-The
monostable multivibrator

## Slide 3: Introduction
There are two different approaches for the generation of sinusoids, most commonly used for the standard waveforms:
  Employing a positive-feedback loop that consists an amplifier and an RC or LC frequency-selective network. It generates sine waves utilizing resonance phenomena, are known as linear oscillators (Section 17.1-3)
  Circuits that generate square, triangular, pulse waveforms are called non-linear oscillators or function generators
      The bistable multivibrator(Section 17.4)
      the astable multivibrator (Section 17.5)
      the monostable multivibrator(Section 17.6)
  A sine wave is obtained by appropriate shaping a triangular waveform

## Slide 4: The basic structure of sinusoidal oscillators
The basic
structure
Amplifier circuit: realize the energy control
Frequency-selective network : oscillator frequency is determined
Positive feedback loop :
amplitude control : implementation of the nonlinear amplitude-stabilization mechanism
A positive-feedback loop is formed by an amplifier and frequency-selective network

## Slide 5: The basic structure of sinusoidal oscillators
Feedback signal xf is summed with a positive sign
The gain-with-feedback (Transfer function) is
 At ω0 the phase of the loop gain should be zero and the magnitude of the loop gain should be unity. (Barkhausen criterion)
For the circuit to produce sustained oscillations at a frequency ω0 the characteristic equation has to have roots at s = ± ω0.
 Barkhausen criterion:
The phase of loop gain should be zero at 0 .
The magnitude of the loop gain should be unity at 0 .
The characteristic equation has roots at s = ± j0 .

## Slide 6: Oscillator
Linear region of the circuit: linear oscillation
Nonlinear region of the circuit: amplitude stabilization

## Slide 7: Nonlinear Amplitude Control

## Slide 8: The implementation of the nonlinear amplitude-stabilization mechanism
The first approach makes use of a limiter circuit
The other mechanism for amplitude control utilizes an element whose resistance can be controlled by the amplitude of the output sinusoid.

## Slide 9: A Popular Limiter Circuit for Amplitude Control
When vi is close to zero:
Linear portion: (linear region)
Figure 17.3 (a) A popular limiter circuit.
Notes: consider first the case of a small (close to zero) input signal vI and a small output voltage vO, so that vA is positive and vB is negative.

## Slide 10: A Popular Limiter Circuit for Amplitude Control
When vi goes positive,D1 is on, D2 is off
Figure 17.3 (a) A popular limiter circuit.
the negative limiting level
the positive limiting level

## Slide 11: A Popular Limiter Circuit for Amplitude Control
Fig. 17.3 (b) Transfer characteristic of the limiter circuit;
When Rf is removed, the limiter turns into a comparator with the characteristic shown Figure 17.3 (c).
Figure 17.3
Figure 17.3

## Slide 12: Oscillator Circuits
Op Amp-RC Oscillator Circuits
  The Wien-Bridge Oscillator
  The phase-Shift Oscillator
LC-Tuned Oscillator
  Colpitts oscillator
  Hareley oscillator
Crystal Oscillator

## Slide 13: The Wien-Bridge Oscillator
Fig. 17.4: A Wien-bridge oscillator without amplitude stabilization.

## Slide 14
Example: The Wien-Bridge Oscillator
Example: Determine C1 and R1 if R2 = 10k, C2 = 0.1µF, R3 = 10k, R4 = 1k in the Wien bridge oscillator shown has an output frequency of 1kHz.

## Slide 15: The Wien-Bridge Oscillator
Fig. 17.5: A Wien-bridge oscillator with a limiter used for amplitude control.

## Slide 16
Fig. 17. 6: Wien-bridge oscillator with an alternative method for amplitude stabilization

## Slide 17: The Phase-Shift Oscillator
The basic structure of the phase-shift oscillator
It consists of a negative-gain amplifier (−K ) with a three-section (third-order) RC ladder network in the feedback.
The circuit oscillates at the frequency for which the phase shift of the RC network is 180.
Only at this frequency will the total phase shift around the loop be 0 or 360.

## Slide 18: The Phase-Shift Oscillator
Fig. 17.8: A practical phase-shift oscillator with a limiter for amplitude stabilization.
To start oscillations, Rf has to be made slightly greater
than the minimum required value. Although the circuit
stabilizes more rapidly, and provides sine waves with
more stable amplitude, if Rf is made much larger than this
minimum, the price paid is an increased output distortion.

## Slide 19
The Phase-Shift Oscillator
R = 1k

## Slide 20
The Phase-Shift Oscillator
BJT Phase-Shift Oscillator

## Slide 21
The Phase-Shift Oscillator
R = 10k, Ri = 1k

## Slide 22: Quadrature Oscillator
Figure 17.9 (a) A quadrature-oscillator circuit. (b) Equivalent circuit at the input of op amp 2.
vo2
vo1
v=vo2/2
v
Decreasing Rf to ensure that oscillation starts
Too much positive feedback results in higher output distortion

## Slide 23: Quadrature Oscillator
The name quadrature oscillator is used because the circuit provides two sinusoids with 90° phase difference.

## Slide 24: Active-Filter Tuned Oscillator
Figure 17.10 Block diagram of the active-filter-tuned oscillator.
Assume the oscillations have already started. The output of the band-pass filter will be a sine wave whose frequency is equal to the center frequency of the filter.
The sine-wave signal is fed to the limiter and then produces a square wave.
 The circuit consists of a high-Q bandpass filter connected in a positive-feedback loop with a hard limiter.
 Any filter circuit with positive gain can be used to implement the bandpass filter.
 Can generate high-quality output sine waves.
 Have independent control of frequency, amplitude and distortion of the output sinusoid.
Op amp-RF oscillators ~ 10 to 100kHz.

## Slide 25: Active-Filter Tuned Oscillator
Fig. 17.11 A practical implementation of the active-filter tuned oscillator

## Slide 26: LC AND CRYSTAL OSCILLATORS

## Slide 27: The LC-Tuned oscillator
Colpitts Oscillator
A parallel LC resonator connected between collector and base.
Feedback is achieved by way of a capacitive divider
Oscillating frequency is determined by the resonance frequency.
(capacitive divider feedback)
For higher frequencies (> 1MHz)

## Slide 28: The LC-Tuned oscillator
Hartley Oscillator
A parallel LC resonator connected between collector and base.
Feedback is achieved by way of an inductive divider.
Oscillating frequency is determined by the resonance frequency.
(inductive divider feedback)
For higher frequencies (> 1MHz)

## Slide 29: The LC-Tuned oscillator
Analysis of Equivalent circuit of the Colpitts oscillator
 LC-tuned oscillators utilize the nonlinear transistor I-V characteristics for amplitude control (self-limiting).
 Collector (drain) current waveforms are distorted due to the nonlinear characteristics.
 Output voltage is a sinusoid with high purity because of the filtering action of the LC tuned circuit.

## Slide 31: The LC-Tuned oscillator
Fig. 17.14 Complete circuit for a Colpitts oscillator
Radio frequency choke (RFC)

## Slide 32: The LC-Tuned oscillator
Colpitts Oscillators: BJT; FET; and IC Based

## Slide 33
The LC-Tuned oscillator
Hartley Oscillator: Used in radio receivers and transmitters More stable than Armstrong oscillators Radio frequency choke (RFC)

## Slide 34
Crystal Oscillators
Crystal is a piezo-electric device which converts mechanical pressure to electrical voltage or vice-versa
Radio communications, broadcasting stations
Piezoelectric effect
Why are crystal oscillators used in many commercial transmitters?

## Slide 35: LC-tuned oscillators –Crystal Oscillators
Fig. 17.15 A piezoelectric crystal. (a) Circuit symbol. (b) Equivalent circuit. (c) Crystal reactance versus frequency [note that, neglecting the small resistance r, Zcrystal = jX(ω)].
Piezoelectric crystal (is high-Q device)

## Slide 36
LC-tuned oscillators –Crystal Oscillators

## Slide 37: LC-tuned oscillators –Crystal Oscillators
A Colpotts (or Pierce) crystal oscillator utilizing a CMOS inverter as an amplifier

## Slide 38: An Application of Crystal Oscillator
Crystals are fabricated by cutting the crude quartz in a very exacting fashion. The type of cut determines the crystal’s natural resonant frequency as well as it’s temperature coefficient.
Crystal are available at frequencies about 15kHz and up providing the best frequency stability. However above 100MHz, they become so small that handling becomes a problem.
Two crystals producing two different frequencies for measuring temperature Timing devices
A miniature 16 MHz quartz crystal enclosed in a hermetically sealed HC-49/S package, used as the resonator in a crystal oscillator.

## Slide 39: Bistable Multivibrators
Another type of waveform generating circuits is the nonlinear oscillators or function generators which uses multivibrators.
A bistable multivibrator has 2 stable states. The circuit can remain in either state indefinitely and changes to the other one only when triggered.
Figure 17.18 A physical analogy for the operation of the bistable circuit. The ball cannot remain at the top of the hill for any length of time (a state of unstable equilibrium or metastability); the inevitably present disturbance will cause the ball to fall to one side or the other, where it can remain indefinitely (the two stable states).
Figure 17.17 A positive-feedback loop capable of bistable operation.

## Slide 40: Bistable Circuit -- three basic factors
The output signal only has two states: positive saturation(L+) and negative saturation(L-).
The circuit can remain in either state indefinitely and move to the other state only when appropriate triggered.(threshold voltage)
The direction of one stage moving to the other stage.
A positive feedback loop capable of bistable operation.

## Slide 41: Bistable Circuit
The bistable circuit (positive feedback loop)
The negative input terminal of the op amp connected to an input signal vI.
Figure 17.19 (a) The bistable circuit of Fig. 17.17 with the negative input terminal of the op amp disconnected from ground and connected to an input signal vI.
Transfer Characteristics of the Inverting Bistable Circuit

## Slide 42: Bistable Circuit
The transfer characteristic of the circuit in (a) for increasing vI.
Positive saturation L+ and negative saturation L-
Figure 17.19 (b) The transfer characteristic of the circuit in (a) for increasing vI. (c) The transfer characteristic for decreasing vI.
The transfer characteristic for decreasing vI.
The complete transfer characteristics.
Trigger signal
Transfer Characteristics of the Inverting Bistable Circuit

## Slide 43: A Bistable Circuit with Noninverting Transfer Characteristics
The transfer characteristic is noninverting.
Figure 17.20 A bistable circuit derived from the positive-feedback loop of Fig. 17.17 by applying vI through R1.

## Slide 44: Application of Bistable Circuit as a Comparator
Comparator is an analog-circuit building block used in a variety applications.
To detect the level of an input signal relative to a preset threshold value.
To design A/D converter.
Include single threshold value and two threshold values.
Hysteresis comparator can reject the interference.

## Slide 45: Application of Bistable Circuit as a Comparator
Figure 17.21 (a) Block diagram representation and transfer characteristic for a comparator having a reference, or threshold, voltage VR. (b) Comparator characteristic with hysteresis.

## Slide 46: Application of Bistable Circuit as a Comparator
Illustrating the use of hysteresis in the comparator characteristics as a means of rejecting interference.
To design a circuit that detects and counts the zero crossings of an arbitrary waveform, a comparator whose threshold is set to 0 can be used. The comparator provides a step change at its output every time zero crossing occurs.

## Slide 47: Bistable Circuit with More Precise Output Level
For this circuit L+ = VZ1 + VD and L– = –(VZ2 + VD), where VD is the forward diode drop.
Fig. 17.23: Limiter circuits are used to obtain more precise output levels for the bistable circuit.
For this circuit L+ = VZ + VD1 + VD2 and L– = –(VZ + VD3 + VD4).

## Slide 48: Generation of Square Waveforms
Fig. 17. 24: (a) Connecting a bistable multivibrator with inverting transfer characteristics in a feedback loop with an RC circuit results in a square-wave generator. (b) The circuit obtained when the bistable multivibrator is implemented with the positive feedback loop circuit.
Operation of the Astable Multivibrator

## Slide 49: Generation of Square Waveforms
Fig. 17. 24: (b) The circuit obtained when the bistable multivibrator is implemented with the positive feedback loop circuit.

## Slide 50
Fig. 17. 24: (c) Waveforms at various nodes of the circuit in (b).
This circuit is called an astable multivibrator.
Time period T = T1+T2

## Slide 51: Generation of Triangle Waveforms
Triangular waveforms can be obtained by replacing the low-pass RC circuit with an integrator. Since the integrator is inverting, the inverting characteristics of the bistable circuit is required.
Fig. 17. 25: A general scheme for generating triangular & square waveforms

## Slide 52: Exercise 17.2
For the circuit of Fig. 17.3(a) with V = 15 V, R1 = 30 kΩ, Rf = 60 kΩ, R2 = R5 = 9 kΩ, and R3 = R4 = 3 kΩ, find the limiting levels and the value of vI at which the limiting levels are reached. Also determine the limiter gain and the slope of the transfer characteristic in the positive and negative limiting regions. Assume that VD = 0.7 V.
Figure 17.3 (a) A popular limiter circuit.

## Slide 53: Exercise 17.2 – Sol.
We have:
=
=
Limiter gain = - Rf / R1 = - 60 / 30 = - 2 V/V
Slope in the limiting regions:

## Slide 54: Exercise 17.3
For the circuit in Fig. 17.5: (a) Disregarding the limiter circuit, find the location of the closed-loop poles. (b) Find the frequency of oscillation. (c) With the limiter in place, find the amplitude of the output sine wave (assume that the diode drop is 0.7 V).
Figure 17.5 A Wien-bridge oscillator with a limiter used for amplitude control.

## Slide 55: Exercise 17.3 – Sol.
The loop gain
=
=
With R = 10k & C = 16 nF
The closed loop poles are found by setting L(s) =1, that is, they are the values of s,

## Slide 56: Exercise 17.3 – Sol.
(b) The frequency of oscillation is 105/16 rad/s or 1 kHz
(c) Refer to Fig., at the positive peak Vo, the voltage at node b will be one diode drop (0.7V) above the voltage Vi which is about 1/3 of Vo.
Thus Vb = 0.7 + Vo/3.
Now, if we neglect the current through D2 in comparison with the currents through R5 & R6 we find that:
From symmetry, we see that the negative peak is equal to the positive peak. Thus the output peak-to-peak voltage is 21.36 V
3