## Slide 1: AVR Assembly compile to Hex (Example 1)
ldi r16, 0x20
out DDRB, r16 // set PB5 to output
loop:
out PINB, r16 // toggle PB5
ldi r17, 0xff
wait:
dec r17
brne wait
rjmp loop
Exercise 1: Convert Following AVR Assembly to Binary code then machine hexa code:

## Slide 2: AVR Assembly compile to Hex (Example 2)
Exercise 2: Convert Following AVR Assembly to Binary code then machine hexa code:
.include "m32def.inc"
.org 0
rjmp main
main:
ldi r16, 0x20
out DDRB, r16
sbi PORTB, 6
loop_main:
sbis PINB, 6
rjmp button_led
cbi PORTB, 5
rjmp loop_main
button_led:
sbi PORTB, 5
rjmp loop_main

## Slide 3: AVR Assembly compile to Hex (Example 3)
Exercise 3: Convert Following AVR Assembly to Binary code then machine hexa code:
LDI R22, 0xFF
OUT DDRB, R22
OUT DDRD, R22
LDI R24,0x00
OUT DDRC,R24
LDI R20,0xB5
loop: IN R18, PINC
OUT PORTB, R18
CPI R18,0xAA
BREQ Check
DEC R20
rjmp loop
Check: LDI R25,0x55
OUT PORTB,R25
rjmp loop