## Slide 1
MICRO-PROCESSING SYSTEM
International University
Vo Minh Thanh, M.Eng
School Of Electrical Engineering
Lecture 7A: AVR Programming in C Part 2

## Slide 2: ATmega16/mega32 pinout
Vital Pins:
  Power
    VCC
    Ground
  Crystal
    XTAL1
    XTAL2
  Reset
I/O pins
  PORTA, PORTB, PORTC, and PORTD
Internal ADC pins
  AREF, AGND, AVCC
+5 V
+5 V
+5 V

## Slide 3: I/O Ports in AVR
ATmega32 is 40-pin chip
A total of 32 pins are
set aside for the 4 ports
PORTA, PORTB, PORTC, PORTD.
Each port has 3 I/O reg-
isters associated with it
They are designated as
DDRx (Data Direction Reg-
ister), PORTx(Data Reg-
ister), and PINx(Port INput pins).
For example, for Port B we have PORTB, DDRB, PINB registers.
each of the I/O registers is 8 bits wide, and each port has a maximum of 8 pins.

## Slide 4: The structure of IO pins

## Slide 5: I/O Ports in AVR
Port | Address | Usage | Port | Address | Usage
PORTA | $3B | Output | PORTC | $35 | Output
DDRA | $3A | Direction | DDRC | $34 | Direction
PINA | $39 | Input | PINC | $33 | Input
PORTB | $38 | Output | PORTD | $32 | Output
DDRB | $37 | Direction | DDRD | $31 | Direction
PINB | $36 | Input | PIND | $30 | Input

## Slide 6: Data Direction Register ( DDRx )
DDRx register is used for the purpose of making a given port an input or output port.
Setting (writing a one) to a bit in the DDRx configures the pin as an Output.
Clearing (writing a zero) to a bit in the DDRx configures the pin as an Input. e.g.
Imagine a person who has 0 dollars, he can only get money, not give it. Similarly when DDR contains 0’s the port gets data.
DDRC = 0xFF;
// Configure PRTC as output
DDRA = 0x00;
// Configure PRTA for input

## Slide 7: Port Input Pin Register ( PINx )
To read the data present at the pins, we should read the PINx register.
To send data out to pins we use the PORTx register .
There is a pull-up resistor for each of the AVR pins.
Different States of a Pin in the AVR Microcontroller |  | 
PORTx | DDRx | 
 | 0 | 1
0 | Input & high impedance | Out 0
1 | Input & Pull-up | Out 1

## Slide 8: Data Register ( PORTx )
The PORTx register controls if the pull-up is activated or not
Writing a 1 to the PORTx register will activate the internal pull-up resistor
Writing a 0 to the PORTx register will deactivate or turn off the internal pull-up resistor
DDRA = 0x00;
//configure PORTA for input
PORTA = 0xFF;
//turn-on the pull-up resistors

## Slide 9: I/O PROGRAMMING IN C: Example 7-9
// LEDs are connected to pins of Port B. Write an AVR C
// program that shows the count from 0 to FFH (0000 0000
// to 1111 1111 in binary) on the LEDs.
#include <avr/io.h>
int main(void)
{
DDRB = 0xFF;
while (1)
{
PORTB = PORTB + 1;
}
return 0;
}

## Slide 10: I/O PROGRAMMING IN C: Example 7-10
// Write an AVR C program to get a byte of data from Port
// B, and then send it to Port C.
#include <avr/io.h> // standard AVR header
int main(void){
unsigned char temp;
DDRB = 0x00; // Port B is input
DDRC = 0xFF; // Port C is output
while(1){
temp = PINB;
PORTC = temp;
}
return 0;
}

## Slide 11: I/O PROGRAMMING IN C: Example 7-11
// Write an AVR C program to get a byte of data from
// Port C. If it is less than 100, send it to Port B;
// otherwise, send it to Port D.
#include <avr/io.h> //standard AVR header
int main(void){
DDRC = 0x00; //Port C is input
DDRB = 0xFF; //Port B is output
DDRD = 0xFF; //Port D is output
PORTC = 0xFF; // activate pullups
unsigned char temp;
while(1){
temp = PINC; //read from PINB
if(temp < 100 )
PORTB = temp;
else
PORTD = temp;
}
return 0;
}

## Slide 12: BITWISE OPERATIONS IN C: Example 7-12
// Run the following program on your simulator and examine
// the results.
#include <avr/io.h> //standard AVR header
int main(void) {
DDRA = 0xFF; //make Port A output
DDRB = 0xFF; //make Port B output
DDRC = 0xFF; //make Port C output
DDRD = 0xFF; //make Port D output
PORTA = 0x35 & 0x0F; // bitwise AND
PORTB = 0x04 | 0x68; // bitwise OR
PORTC = 0x54 ^ 0xF0; // bitwise XOR
PORTD = ~ 0x55; // bitwise NOT
while(1);
return 0;
}

## Slide 13: BITWISE OPERATIONS IN C: Example 7-13
// Write an AVR C program to toggle only bit 4 of Port B
// continuously without disturbing the rest of the pins of
// Port B.
#include <avr/io.h> //standard AVR header
int main(void)
{
DDRB = 0xFF; //PORTB is output
while(1)
{
PORTB = PORTB ^ 0b00010000;
//set bit 4 (5th bit) of PORTB
}
return 0;
}

## Slide 14: BITWISE OPERATIONS IN C: Example 7-14
// Write an AVR C program to monitor bit 5 of port C. If
// it is HIGH, send 55H to Port B; otherwise, send AAH to
// Port B.
#include <avr/io.h> // standard AVR header
int main(void){
DDRB = 0xFF; // PORTB is output
DDRC = 0x00; // PORTC is input
while(1){
if (PINC & 0b00100000) // check bit 5 (6th bit)
// of PINC
PORTB = 0x55;
else
PORTB = 0xAA;
}
return 0;
}

## Slide 15: BITWISE OPERATIONS IN C: Example 7-15
// A door sensor is connected to bit 1 of Port B, and an
// LED is connected to bit 7 of Port C. Write an AVR C
// program to monitor the door sensor and, when it opens,
// turn on the LED.
#include <avr/io.h> //standard AVR header
int main(void){
DDRB = DDRB & 0b11111101; //pin 1 of Port B is input
DDRC = DDRC | 0b10000000; //pin 7 of Port C is output
while(1){
if (PINB & 0b00000010)//check pin 1(2nd pin) of PINB
PORTC = PORTC | 0b10000000;
//set pin 7 (8th pin) of PORTC
else
PORTC = PORTC & 0b01111111;
//clear pin 7 (8th pin) of PORTC
}
return 0;
}

## Slide 16: BITWISE OPERATIONS IN C: Example 7-16
// The data pins of an LCD are connected to Port B. The
// information is latched into the LCD whenever its Enable
// pin goes from HIGH to LOW. The enable pin is connected
// to pin 5 of Port C (6th pin). Write a C program to send
// "The Earth is but One Country" to this LCD.
#include <avr/io.h> //standard AVR header
int main(void){
unsigned char message[] = "The Earth is but One Country";
unsigned char z;
DDRB = 0xFF; //Port B is output
DDRC = DDRC | 0b00100000; //pin 5 of Port C is output
for ( z = 0; z < 28; z++){
PORTB = message[z] ;
PORTC = PORTC | 0b00100000; //pin LCD_EN of Port C is 1
PORTC = PORTC & 0b11011111; //pin LCD_EN of Port C is 0
}
while (1); return 0;
} //In Chapter 12 we will study more about LCD interfacing

## Slide 17: BITWISE OPERATIONS IN C: Example 7-17
// Write an AVR C program to read pins 1 and 0 of Port B
// and issue an ASCII character to Port D
#include <avr/io.h> //standard AVR header
int main(void){
unsigned char z;
DDRB = DDRB & 0b11111100 ; // make Port B an input
DDRD = 0xFF; // make Port D an output
while(1){ // repeat forever
z = PINB; // read PORTB
z = z & 0b00000011; // mask the unused bits
switch(z){ // make decision
case(0): PORTD = '0'; break; // issue ASCII 0
case(1): PORTD = '1'; break; // issue ASCII 1
case(2): PORTD = '2'; break; // issue ASCII 2
case(3): PORTD = '3'; break; // issue ASCII 3
}
}
return 0;
}

## Slide 18: BITWISE OPERATIONS IN C: Example 7-18
// Write an AVR C program to monitor bit 7 of Port B. If
// it is 1 make bit 4 of Port B input; otherwise, change
// pin 4 of Port B to output.
#include <avr/io.h> //standard AVR header
int main(void){
DDRB = DDRB & 0b01111111; //bit 7 of Port B is input
// DDRB &= 0b01111111;
while (1){
if(PINB & 0b10000000)
//bit 4 of Port B is input
DDRB = DDRB & 0b11101111;
// DDRB &= 0b11101111;
else
//bit 4 of Port B is output
DDRB = DDRB | 0b00010000;
// DDRB |= 0b00010000;
}
return 0;
}

## Slide 19: BITWISE OPERATIONS IN C: Example 7-19
// Write an AVR C program to get the status of bit 5 of
// Port B and send it to bit 7 of port C continuously.
#include <avr/io.h> //standard AVR header
int main(void){
DDRB = DDRB & 0b11011111; // bit 5 of Port B is input
// DDRB &= 0b11011111; // using compound Assignment
DDRC = DDRC | 0b10000000; // bit 7 of Port C is output
// DDRC |= 0b10000000; // using compound Assignment
while (1){
if(PINB & 0b00100000) //set bit 7 of Port C to 1
PORTC = PORTC | 0b10000000;
PORTC |= 0b10000000;
else //clear bit 7 of Port C to 0
PORTC = PORTC & 0b01111111;
PORTC &= 0b01111111;
}
return 0;
}

## Slide 20: BITWISE OPERATIONS IN C: Example 7-20
// Write an AVR C program to toggle all the pins of
// Port B continuously.
#include <avr/io.h> // standard AVR header
int main(void){
DDRB = 0xFF; // Port B is output
PORTB = 0xAA;
while(1)
{ PORTB = ~ PORTB; } // toggle PORTB
return 0;
}
#include <avr/io.h> // standard AVR header
int main(void){
DDRB = 0xFF; PORTB = 0xAA; // Port B is output
while(1)
PORTB = PORTB ^ 0xFF;
return 0;
}

## Slide 21: Bitwise Shift Operators in C: Example 7-23
// Write an AVR C program to monitor bit 7 of Port B. If
// it is 1, make bit 4 of Port B input; else, change pin
// 4 of Port B to output.
#include <avr/io.h> // standard AVR header
int main(void) {
DDRB = DDRB & ~(1<<7); // bit 7 of Port B is input
while (1){
if(PINB & (1<<7)) // if bit 7 of Port B is 1
DDRB = DDRB & ~(1<<4);// bit 4 of Port B is input
else
DDRB = DDRB | (1<<4); //bit 4 of Port B is output
}
return 0;
}

## Slide 22: Bitwise Shift Operators in C: Example 7-24
// Write an AVR C program to get the status of bit 5 of
// Port B and send it to bit 7 of port C continuously.
#include <avr/io.h> // standard AVR header
int main(void){
DDRB = DDRB & ~(1<<5); // bit 5 of Port B is input
DDRC = DDRC | (1<<7); // bit 7 of Port C is output
while (1){
if(PINB & (1<<5))
// set bit 7 of Port C to 1
PORTC = PORTC | (1<<7);
else
// clear bit 7 of Port C to 0
PORTC = PORTC & ~(1<<7);
}
return 0;
}

## Slide 23: Bitwise Shift Operators in C: Example 7-25
// A door sensor is connected to the port B pin 1, and an
// LED is connected to port C pin 7. Write an AVR C
// program to monitor the door sensor and, when it opens,
// turn on the LED.
#include <avr/io.h> // standard AVR header
#define LED 7
#define SENSOR 1
int main(void){
DDRB = DDRB & ~(1<<SENSOR); // SENSOR pin is input
DDRC = DDRC | (1<< LED); // LED pin is output
while(1){
if(PINB & (1<<SENSOR)) // check SENSOR pin of PINB
// set LED pin of Port C
PORTC = PORTC | (1<<LED);
else
// clear LED pin of Port C
PORTC = PORTC & ~(1<<LED);
}
return 0;
}

## Slide 24: Data Conversion Programs in C: Example 7-26
// Write an AVR C program to convert packed BCD 0x29 to
// ASCII and display the bytes on PORTB and PORTC.
#include <avr/io.h> // standard AVR header
int main(void){
unsigned char x, y;
unsigned char mybyte = 0x29;
DDRB = DDRC = 0xFF; // make Ports B and C output
x = mybyte & 0x0F; // mask upper 4 bits
PORTB = x | 0x30; // make it ASCII
y = mybyte & 0xF0; // mask lower 4 bits
y = y >> 4; // shift it to lower 4 bits
PORTC = y | 0x30; // make it ASCII
while(1); // stay here
return 0;
}

## Slide 25: Data Conversion Programs in C: Example 7-27
//Write an AVR C program to convert ASCII digits of '4‘
// and '7' to packed BCD and display them on PORTB.
#include <avr/io.h> //standard AVR header
int main(void){
unsigned char bcdbyte;
unsigned char w = '4';
unsigned char z = '7';
DDRB = 0xFF; // make Port B an output
w &= 0x0F; // mask 3
w <<= 4; // shift left to make upper BCD digit
z &= 0x0F; // mask 3
bcdbyte = w | z; // combine to make packed BCD
PORTB = bcdbyte;
while(1);
return 0;
}

## Slide 26: Data Conversion Programs in C: Exercise
// Write an AVR C program to take two BCD numbers 0x74
// from PORTC. Swap these numbers to 0x74 and show the
// result on PORTC
#include <avr/io.h> //standard AVR header
int main(void){
unsigned char c,d,e;
DDRC = 0x00; // PORTC is input port
DDRB = 0xFF; // PORTB is output port
while(1){
c = PINC; // take input 0x74
d = c & 0x0F; // d = 0x04
e = c & 0xF0; // e = 0x70
d = d << 4; // d = 0x40
e = e >> 4; // d = 0x07
PORTB = d|e; // PORTB = 0x47
}
return 0; }

## Slide 27: Data Conversion Programs in C: Example 7-31
// Write an AVR C program to convert 11111101 (FD hex) to
// decimal and display the digits on PORTB, PORTC, PORTD.
#include <avr/io.h> //standard AVR header
int main(void){
unsigned char x, binbyte, d1, d2, d3;
DDRB = DDRC = DDRD = 0xFF; // Ports B, C and D are output
binbyte = 0xFD; // binary (hex) byte
x = binbyte / 10; // divide by 10
d1 = binbyte % 10; // find remainder (LSD)
d2 = x % 10; // middle digit
d3 = x / 10; // most-significant digit(MSD)
PORTB = d1;
PORTC = d2;
PORTD = d3;
while(1);
return 0;
}

## Slide 28: Data Types Conversion Functions in C
stdlib.h header file has some useful functions to convert integer to string or string to integer.
Function Name | Description
int atoi(char *str) | Converts the string str to integer
long atol(char *str) | Converts the string str to long
void itoa(int n, char *str) | Converts the integer n to characters in string str
void ltoa(int n, char *str) | Converts the long n to characters in string str
float atof(char *str) | Converts the characters from string str to float

## Slide 29: Accessing EEPROM in AVR
Every member of the AVR microcontrollers has some amount of on-chip EEPROM.
The data in SRAM will be lost if the power is disconnected.
EEPROM memory can save stored data even when the power is cut off.
The Size of EEPROM in different AVR Micro-controllers is given below
Chip | Bytes | Chip | Bytes | Chip | Bytes
ATmega8 | 512 | ATmega 16 | 512 | ATmega32 | 1024
ATmega64 | 2048 | ATmegal28 | 4096 | ATmega256RZ | 4096
ATmega640 | 4096 | ATmegal280 | 4096 | ATmega2560 | 4096

## Slide 30: EEPROM Registers
There are three I/O registers that are directly related to EEPROM. These are
  EECR (EEPROM Control Register)
  EEDR (EEPROM Data Register)
  EEARH-EEARL (EEPROM Address Register High-Low)
EEPROM Data Register (EEDR)
To Read/write data to EEPROM, you have to Read/write to the EEDR register.
EEPROM Address Register (EEARH and EEARL)
The EEARH:EEARL registers together make a 16-bit register to address each location in EEPROM memory space.
When you want to read from or write to EEPROM, you should load the EEPROM location address in EEAR.

## Slide 31: EEPROM Registers
Only 10 bits of the EEAR registers are used in ATmega32. Because ATmega32 has 1024-byte EEPROM locations,
ATmega16 has 512 bytes of EEPROM So 9 bits of the EEAR registers are used
EEPROM Control Register (EECR)
The EECR register is used to select the kind of operation to perform on. The operation can be start, read, and write.
Bit | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 
EEARH | - | - | - | - | - | - | EEAR9 | EEAR8 | 
EEARL | EEAR7 | EEAR6 | EEAR5 | EEAR4 | EEAR3 | EEAR2 | EEAR1 | EEAR0 | 
Bit | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | 
Figure 6-15: EEPROM Address Register |  |  |  |  |  |  |  |  | 

## Slide 32: EEPROM Registers
The bits of the EECR register are as follows:
EEPROM Read Enable (EERE): Setting this bit to one will cause a read operation if EEWE is zero. When a read operation starts, one byte of EEPROM will be read into the EEPROM Data Register (EEDR). The EEAR register specifies the address of the desired byte.
EEPROM Write Enable (EEWE) and EEPROM Master Write Enable (EEMWE): When EEMWE is set,then within four clock cycles setting EEWE will start a write operation. If EEMWE is zero, setting EEWE to one will have no effect.
EECR | - | - | - | - | EERIE | EEMWE | EEWE | EERE | 
Bit | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | 
Figure 6-16: EEPROM Control Register |  |  |  |  |  |  |  |  | 

## Slide 33: EEPROM Registers
The When you set EEMWE to one, the hardware clears the bit to zero after four clock cycles. This prevents unwanted write operations on EEPROM contents.
Notice that you cannot start read or write operations before the last write operation is finished. You can check for this by polling the EEWE bit. If EEWE is zero it means that EEPROM is ready to start a new read or write operation.
EEPROM Ready Interrupt Enable (EERIE): This will be explained in Chapter 10. In Figure 6-16, bits 4 to 7 of EECR are unused at the present time and are reserved.

## Slide 34: Programming the AVR to write on EEPROM
To write on EEPROM the following steps should be followed. Notice that steps 2 and 3 are optional, and the order of the step 2 and 3 is not important. Also note that you cannot do anything between step 4 and step 5 because the hardware clears the EEMWE bit to zero after four clock cycles.
  Wait until EEWE becomes zero.
  Write new EEPROM address to EEAR (optional).
  Write new EEPROM data to EEDR (optional).
  Set the EEMWE bit to 1, and Within four clock cycles after setting EEMWE, set EEWE to one.
  Wait until EEWE becomes zero.

## Slide 35: EEPROM Access in C: Example 7-36
// Write an AVR C program to store ‘a' into location
// Ox005F of EEPROM.
#include <avr/io.h> //standard AVR header
void EEPROM_write(unsigned int Address, unsigned char Data){
// Wait for completion of previous write
while(EECR & (1<<EEWE));
// Set up address and data registers
EEAR = Address; EEDR = Data;
// Write logical one to EEMWE
EECR |= (1<<EEMWE);
// Start eeprom write by setting EEWE
EECR |= (1<<EEWE);
} int main(void){
EEPROM_write(0x5F, 'a'); while(1); return 0;}

## Slide 36: EEPROM Access in C: Example 7-37
// Write an AVR C program to read the content of location
// 0x005F of EEPROM into PORTB.
#include <avr/io.h> //standard AVR header
unsigned char EEPROM_read(unsigned int Address){
// Wait for completion of previous write
while(EECR & (1<<EEWE));
// Set up address register
EEAR = Address;
// Start eeprom read by writing EERE
EECR |= (1<<EERE);
// Return data from data register
return EEDR;
}
int main(void){
DDRB = 0xFF;
PORTB = EEPROM_read(0x5F);
while(1);
return 0;
}

## Slide 37: Reading and Writing EEPROM in C (1/2)
// Write an AVR C program to store ‘a' into location
// Ox005F of EEPROM then read from EEPROM.
#include <avr/io.h> //standard AVR header
void EEPROM_write
(unsigned int Address, unsigned char Data)
{
// Wait for completion of previous write
while(EECR & (1<<EEWE));
// Set up address and data registers
EEAR = Address; EEDR = Data;
// Write logical one to EEMWE
EECR |= (1<<EEMWE);
// Start eeprom write by setting EEWE
EECR |= (1<<EEWE);
}
unsigned char EEPROM_read(unsigned int Address)
{
// Wait for completion of previous write
while(EECR & (1<<EEWE));

## Slide 38: Reading and Writing EEPROM in C (2/2)
// Set up address register
EEAR = Address;
// Start eeprom read by writing EERE
EECR |= (1<<EERE);
// Return data from data register
return EEDR;
}
int main(void)
{
unsigned char data = 0x33;
DDRB = 0xFF;
EEPROM_write(0x5F, 'a');
data = EEPROM_read(0x5F);
PORTB = data;
while(1);
return 0;
}

## Slide 39: Writing a String on EEPROM
int main(void)
{
unsigned char i;
unsigned char msg[] = "IIUI ISB";
DDRB = 0xFF;
for(i=0 ; msg[i] ; i++)
EEPROM_write(i, msg[i]);
EEPROM_write(i, 0); // Write NULL
PORTB = 0x55;
while(1);
return 0;
}