## Slide 1
MICRO-PROCESSING SYSTEM
International University
Vo Minh Thanh, M.Eng
School Of Electrical Engineering
Lecture 9A:
Serial Interface Tutorial

## Slide 2: Serial Buses in our project
UART serial bus for sending debug messages to your development host
I2C serial bus for communicating with sensors (e.g., the accelerometer)
SPI serial bus for communicating with the Bluetooth Low Energy radio

## Slide 3: Serial Interfaces
Timers
CPU
Software
Hardware
Internal
External
Input
System Buses
AHB/APB
ldr (read)
str (write)
ISA
USART
DAC/ADC
Internal &
External
Memory
GPIO/INT
Output
Interrupt
Compare
Capture
I2C
SPI
UART
ADC
DAC
C
Assembly
Machine Code
Interrupts
interrupts
EMC
SVC#
fault
traps &
exceptions
INT#

## Slide 4: Parallel Bus VS Serial Bus

## Slide 5: Simplistic View of Serial Port Operation
7
6
7
5
6
7
4
5
6
7
3
4
5
6
7
2
3
4
5
6
7
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
n
n+1
n+2
n+3
n+4
n+5
n+6
n+7
n+8
Transmitter
Receiver
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
0
1
2
3
4
5
0
1
2
3
4
0
1
2
3
0
1
2
0
1
0
n
n+1
n+2
n+3
n+4
n+5
n+6
n+7
n+8
Interrupt raised when
Transmitter (Tx) is empty
a Byte has been transmitted
and next byte ready for loading
Interrupt raised when
Receiver (Rx) is full
a Byte has been received
and is ready for reading
Notes: 5

## Slide 6: Serial Bus Interface Motivations
Motivation
  Without using a lot of I/O lines
    I/O lines require I/O pads which cost $$$ and size
    I/O lines require PCB area which costs $$$ and size
  Connect different systems together
    Two embedded systems
    A desktop and an embedded system
  Connect different chips together in the same embedded system
    MCU to peripheral
    MCU to MCU
  Often at relatively low data rates
  But sometimes at higher data rates
So, what are our options?
  Universal Synchronous/Asynchronous Receiver Transmitter
  Also known as USART (pronounced: “you-sart”)

## Slide 7: Serial Bus Design Space
Number of wires required?
Asynchronous or synchronous?
How fast can it transfer data?
Can it support more than two endpoints?
Can it support more than one master (i.e. txn initiator)?
How do we support flow control?
How does it handle errors/noise?
How far can signals travel?

## Slide 8: Serial Bus Examples
 | S/A | Type | Duplex | #Devices | Speed (kbps) | Distance (ft) | Wires
RS232 | A | Peer | Full | 2 | 20 | 30 | 2+
RS422 | A | Multi-drop | Half | 10 | 10000 | 4000 | 1+
RS485 | A | Multi-point | Half | 32 | 10000 | 4000 | 2
I2C | S | Multi-master | Half | ? | 3400 | <10 | 2
SPI | S | Multi-master | Full | ? | >1000 | <10 | 3+
Microwire | S | Master/slave | Full | ? | >625 | <10 | 3+
1-Wire | A | Master/slave | half | ? | 16 | 1000 | 1+

## Slide 9: UART Uses
PC serial port is a UART!
Serializes data to be sent over serial cable
  De-serializes received data
Slides from BYU CS 224

## Slide 10: UART Uses
Used to be commonly used for internet access

## Slide 11: UART
Universal Asynchronous Receiver/Transmitter
Hardware that translates between parallel and serial forms
Commonly used in conjunction with communication standards such as EIA, RS-232, RS-422 or RS-485

## Slide 12: Protocol
Each character is sent as
  a logic low start bit
  a configurable number of data bits (usually 7 or 8, sometimes 5)
  an optional parity bit
  one or more logic high stop bits
  with a particular bit timing (“baud”)

## Slide 13: UART Example
Send the ASCII letter ‘W’ (1010111)

## Slide 14: UART Hardware Connection

## Slide 15: UART Character Reception

## Slide 16: UART Character Reception

## Slide 17: UART Character Reception

## Slide 18: UART Character Reception
Receiver also verifies that stop bit is ‘1’
  If not, reports “framing error” to host system
New start bit can appear immediately after stop bit
  Receiver will resynchronize on each start bit

## Slide 19: Let us design a UART transmitter

## Slide 20: Transmitter/System Handshaking
System asserts Send and holds it high when it wants to send a byte
UART asserts Busy signal in response
When UART has finished transfer, UART de-asserts Busy signal
System de-asserts Send signal

## Slide 21: Transmitter Block Diagram

## Slide 22: Discussion Questions
How fast can we run a UART?
What are the limitations?
Why do we need start/stop bits?
How many data bits can be sent?
  19200 baud rate, no parity, 8 data bits, 1 stop bit

## Slide 23: Serial Peripheral Interconnect (SPI)
Another kind of serial protocol in embedded systems (proposed by Motorola)
Four-wire protocol
  SCLK — Serial Clock
  MOSI/SIMO — Master Output, Slave Input
  MISO/SOMI — Master Input, Slave Output
  SS — Slave Select
Single master device and with one or more slave devices
Higher throughput than I2C and can do “stream transfers”
No arbitration required
But
  Requires more pins
  Has no hardware flow control
  No slave acknowledgment (master could be talking to thin air and not even know it)
Notes: Better suited for “data streams”, i.e. ADC converters
Full duplex capability, i.e. communication between a codec and digital signal processor

## Slide 24: What is SPI?
Serial Bus protocol
Fast, Easy to use, Simple
Everyone supports it

## Slide 25: SPI Basics
A communication protocol using 4 wires
  Also known as a 4 wire bus
Used to communicate across small distances
Multiple Slaves, Single Master
Synchronized

## Slide 26: SPI Capabilities
Always Full Duplex
  Communicating in two directions at the same time
  Transmission need not be meaningful
Multiple Mbps transmission speed
Transfers data in 4 to 16 bit characters
Multiple slaves
  Daisy-chaining possible

## Slide 27: SPI Protocol
Wires:
  Master Out Slave In (MOSI)
  Master In Slave Out (MISO)
  System Clock (SCLK)
  Slave Select 1…N
Master Set Slave Select low
Master Generates Clock
Shift registers shift in and out data

## Slide 28: SPI Wires in Detail
MOSI – Carries data out of Master to Slave
MISO – Carries data from Slave to Master
  Both signals happen for every transmission
SS_BAR – Unique line to select a slave
SCLK – Master produced clock to synchronize data transfer

## Slide 29: SPI uses a “shift register” model of communications
Master shifts out data to Slave, and shifts in data from Slave
http://upload.wikimedia.org/wikipedia/commons/thumb/b/bb/SPI_8-bit_circular_transfer.svg/400px-SPI_8-bit_circular_transfer.svg.png

## Slide 30: SPI Communication

## Slide 31: SPI clocking: there is no “standard way”
Four clocking “modes”
  Two phases
  Two polarities
Master and selected slave must be in the same mode
During transfers with slaves A and B, Master must
  Configure clock to Slave A’s clock mode
  Select Slave A
  Do transfer
  Deselect Slave A
  Configure clock to Slave B’s clock mode
  Select Slave B
  Do transfer
  Deselect Slave B
Master reconfigures clock mode on-the-fly!

## Slide 32: SPI timing diagram
Timing Diagram – Showing Clock polarities and phases
http://www.maxim-ic.com.cn/images/appnotes/3078/3078Fig02.gif

## Slide 33: SPI Pros and Cons
Pros:
  Fast and easy
    Fast for point-to-point connections
    Easily allows streaming/Constant data inflow
    No addressing/Simple to implement
  Everyone supports it
Cons:
  SS makes multiple slaves very complicated
  No acknowledgement ability
  No inherent arbitration
  No flow control

## Slide 34: I2C bus in our projects
Communication with the accelerometer
  Read from the accelerometer
Pros
  Simple wire connection
  Two wires bus that can connect multiple peripherals with the MCU
Cons
  Complexity is significantly higher

## Slide 35: How to operate the camera?
MCU
Accel
I2C
I2C
register 1
register 2
….
Springs
https://www.youtube.com/watch?v=eqZgxR6eRjo

## Slide 36: I2C Details
Two lines
  Serial data line (SDA)
  Serial clock line (SCL)
Only two wires for connecting multiple devices

## Slide 37: I2C Details
Each I2C device recognized by a unique address
Each I2C device can be either a transmitter or receiver
I2C devices can be masters or slaves for a data transfer
  Master (usually a microcontroller): Initiates a data transfer on the bus, generates the clock signals to permit that transfer, and terminates the transfer
  Slave: Any device addressed by the master at that time

## Slide 38: Bit Transfer on the I2C Bus
In normal data transfer, the data line only changes state when the clock is low
SDA
SCL
Data line stable; Data valid
Change of data allowed

## Slide 39: Start and Stop Conditions
A transition of the data line while the clock line is high is defined as either a start or a stop condition.
Both start and stop conditions are generated by the bus master
The bus is considered busy after a start condition, until a stop condition occurs
Start Condition
Stop Condition
SCL
SCL
SDA
SDA

## Slide 40: I2C Addressing
Each node has a unique 7 (or 10) bit address
Peripherals often have fixed and programmable address portions
Addresses starting with 0000 or 1111 have special functions:-
  0000000 Is a General Call Address
  0000001 Is a Null (CBUS) Address
  1111XXX Address Extension
  1111111 Address Extension – Next Bytes are the Actual Address

## Slide 41: I2C-Connected System
Example I2C-connected system with two microcontrollers
(Source: I2C Specification, Philips)

## Slide 42: Master-Slave Relationships
Who is the master?
  master-transmitters
  master-receivers
Suppose microcontroller A wants to send information to microcontroller B
  A (master) addresses B (slave)
  A (master-transmitter), sends data to B (slave-receiver)
  A terminates the transfer.
If microcontroller A wants to receive information from microcontroller B
  A (master) addresses microcontroller B (slave)
  A (master-receiver) receives data from B (slave-transmitter)
  A terminates the transfer
In both cases, the master (microcontroller A) generates the timing and terminates the transfer