## Slide 1: Quiz Week 6

## Slide 2: Use Matlab to perform the quiz
An BCC iron-carbon alloy initially containing 0.2 wt% C is carburized at an elevated temperature and in an atmosphere wherein the surface carbon concentration is maintained at 1.2 wt%. If after 52 h the concentration of carbon is 0.4 wt% at a position 3.0 mm below the surface, determine the temperature at which the treatment was carried out.
Hint: Use table 5.2 to get the diffusion coefficient

## Slide 3: Quiz Continue
For the temperature we have calculated in previous problem. We would like to plot the concentration value of C(x,t) versus Time, for the time from 0 hours to 60 hours at the same location of 3mm.
As we can see, the Carbon concentration value C(3mm,52hours) is 0.4%