## Slide 1
Text book:
Sedra and Smith, “Microelectronic Circuits,” 6th Edition.
Lecture # 4: Frequency Response
International University
School of Electrical Engineering
ANALOG ELECTRONICS

## Slide 3: Transfer function: poles, zeros
Most of our work in this chapter will be concerned with finding amplifier voltage gain as a transfer function of the complex frequency s.
A capacitance C: is equivalent an impedance 1/sC
An inductance L: is equivalent an impedance sL
Voltage transfer function: by replacing s by j, we can obtain its magnitude response and phase response

## Slide 4: Transfer function: poles, zeros
Z1, Z2, … Zm are called the transfer-function zeros or transmission zeros.
P1, P2, … Pn are called the transfer-function poles or natural modes.
The poles and zeros can be either real or complex numbers, the complex poles (zeros) must occur in conjugate pairs.

## Slide 7
First-order Functions
All the transfer functions encountered in this chapter have real poles and zeros and can be written as the product of first-order transfer functions.
ω0, called the pole frequency, is equal to the inverse of the time constant of circuit network (STC).
RC

## Slide 8
Example 1: High pass circuit
RC is the time constant; ωL=1/RC

## Slide 9
Example 2: Low pass circuit
RC is the time constant; ωH = 1/RC

## Slide 10
Bode Plots
A simple technique exists for obtaining an approximate plot of the magnitude and phase of a transfer function given its poles and zeros. The resulting diagram is called Bode plots
A transfer function consists of a product of factors of the form s+a

## Slide 11
Bode Plots
Magnitude of a zero

## Slide 12: Example 3

## Slide 13
The amplifier transfer function
(a) a capacitively coupled amplifier (b) a direct-coupled amplifier

## Slide 14
The Gain Function
Gain function
Midband: No capacitors in effect
Low-frequency band: coupling and bypass capacitors in effect
High-frequency band: transistor internal capacitors in effect

## Slide 15
GENERALIZED CAPACITOR-COUPLED AMPLIFIER
FREQUENCY RESPONSE
2 plots represent DC-coupled (left) and AC-coupled (right) amplifiers. The single transistor amplifiers generally need input & output coupling capacitors so that external DC voltages do not shift the bias point. Thus, these will have AC-coupled responses.
• For the AC-coupled response, near L and below, the amplifier’s response acts like a high-pass filter.
• For both cases, near H and above, the amplifier’s response acts like a low-pass filter.
• The (hopefully) flat region in the middle is the “mid-band.” We typically talk about the “mid-band gain” of an AC-coupled amplifier.
• It is important to note that one can look at the transfer function of an AC-coupled amplifier as the product of the high-pass, mid-band, and low-pass transfer functions,
Reminder: The impedance of a capacitor is
Thus, they are open-circuits at DC and shorts at very high frequencies.

## Slide 16: DOMINANT POLES
Dominant poles are poles that dominate over the others in the transfer function so that the low- or high-frequency response of an amplifier can be approximated as a first-order high- or low-pass filter.
DOMINANT LOW-FREQUENCY POLE
If there is a dominant low-frequency pole (this is the one that acts like a HIGH-PASS filter), the low-frequency response can be approximated as,
So, if the “full” low-frequency response is
this means that P1 is at a much HIGHER frequency than the other poles so that it can DOMINATE...
• Note that the number of poles and zeros must be equal (at that point) if the function “flattens out” in the mid-band!
If there is no dominant pole, we can make the following approximation

## Slide 17
DOMINANT POLES
DOMINANT HIGH-FREQUENCY POLE
If there is a dominant high-frequency pole (this is the one that acts like a LOW-PASS filter), the high-frequency response can be approximated as:
So, if the “full” high-frequency response is
this means that P1 is at a much LOWER frequency than the other poles so that it can DOMINATE...
Note that the number of poles and zeros must be equal (at that point) if the function “flattens out” in the mid-band!
If there is no dominant pole, you can make the following approximation
f

## Slide 18
SHORT-CIRCUIT AND OPEN-CIRCUIT TIME CONSTANT METHODS FOR APPROXIMATING THE RESPONSE OF AMPLIFIERS
This is a very useful method for approximating upper and lower cut-off frequencies, assuming that there is a dominant pole.
Depending on which of the two methods we use, for each capacitor in the circuit, we replace the capacitors in the circuit, except for the one you are looking at, with either shorts or opens.
Two key rules apply to both methods:

## Slide 19
All we have to do is step through the process of calculating a “local” RC time-constant for each capacitor in the circuit.
For each capacitor you set all other capacitances (other than the one you are looking at) to zero (i.e. they become OPEN CIRCUITS as if they have not yet had any effect on the amplifier's roll-off) and determine the resistance, Rio, seen by Ci (the capacitor you are working with).
• Repeat this process for each capacitor.
• The upper cut-off frequency is then approximately given by,
SHORT-CIRCUIT AND OPEN-CIRCUIT TIME CONSTANT METHODS FOR APPROXIMATING THE RESPONSE OF AMPLIFIERS
OPEN-CIRCUIT TIME CONSTANTS FOR UPPER CUT-OFF FREQUENCY APPROXIMATION
This approach can tell you which of the capacitances in a circuit is most significant in determining the high-frequency response!

## Slide 20
SHORT-CIRCUIT AND OPEN-CIRCUIT TIME CONSTANT METHODS FOR APPROXIMATING THE RESPONSE OF AMPLIFIERS
SHORT-CIRCUIT TIME CONSTANTS FOR LOWER CUT-OFF FREQUENCY APPROXIMATION
• Again, all you have to do is step through the process of calculating a “local” RC time-constant for each capacitor in the circuit.
For each capacitor you set all other capacitances (other than the one you are looking at) to INFINITY (i.e. they become SHORT CIRCUITS as if they have already become low enough impedance to neglect) and determine the resistance, RiS, seen by Ci (the capacitor you are working with).
• Repeat this process for each capacitor.
• The lower cut-off frequency is then approximately given by,
This approach can tell you which of the capacitances in a circuit is most significant in determining the low-frequency response!

## Slide 22: Introduction
IN THIS CHAPTER YOU WILL LEARN
  How coupling and bypass capacitors cause the gain of discrete circuit amplifiers to fall off at low frequencies, and how to obtain an estimate of the frequency fL at which the gain decreases by 3dB below its value at midband.
  The internal capacitive effects present in the MOSFET and the BJT and how to model these effects by adding capacitances to the hybrid-p model of each of the two transistor types.
  The high-frequency limitation on the gain of the CS and CE amplifiers and how the gain falloff and the upper 3-dB frequency fH are mostly determined by the small capacitances between the drain and gate (collector and base).

## Slide 23: Introduction
IN THIS CHAPTER YOU WILL LEARN
  Powerful methods for the analysis of the high-frequency response of amplifier circuits of varying complexity.
  How the cascode amplifier studied in Chapter 7 can be designed to obtain wider bandwidth than is possible with CS and CE amplifiers.
  The high-frequency performance of the source and emitter followers.
  The high-frequency performance of differential amplifiers.
  Circuit configurations for obtaining wideband amplification.

## Slide 24: Introduction
Previously assumed that gain is constant and independent of frequency.
  implied that bandwidth was infinite
  this is not true
Middle-frequency band (midband) is the range of frequencies over which device gain is constant.

## Slide 25
Figure 9.1: Sketch of the magnitude of the gain of a discrete-circuit BJT or MOS amplifier versus frequency. The graph delineates the three frequency bands relevant to frequency-response determination.
Midband:
The frequency range of interest for amplifiers
Large capacitors can be treated as short circuit and small capacitors can be treated as open circuit
Gain is constant and can be obtained by small-signal analysis
Amp. bandwidth is defined by fL and fH
BW ≡ fH − fL
Notes: single-time-constant (STC)

## Slide 26
Low-frequency band:
Gain drops at frequencies lower than fL
Large capacitors can no longer be treated as short circuit
The gain roll-off is mainly due to coupling and by-pass capacitors
Figure 9.1: Sketch of the magnitude of the gain of a discrete-circuit BJT or MOS amplifier versus frequency. The graph delineates the three frequency bands relevant to frequency-response determination.

## Slide 27
Figure 9.1: Sketch of the magnitude of the gain of a discrete-circuit BJT or MOS amplifier versus frequency. The graph delineates the three frequency bands relevant to frequency-response determination.
High-frequency band:
Gain drops at frequencies higher than fH
Small capacitors can no longer treated as open circuit
The gain roll-off is mainly due to parasitic capacitances of the MOSFETs and BJTs

## Slide 28: 9.1. Low Frequency Response of the Common-Source and Common-Emitter Amplifiers
Figure 9.2(a) shows a discrete-circuit, common-source amplifier.
  coupling capacitors CC1 and CC2
  bypass capacitor CS
Objective is to determine the effect of these capacitances on gain (Vo/Vsig).
At low frequencies, their reactance (1/jwC) is high and gain is low.
Figure 9.2: (a) Capacitively coupled common-source amplifier.
(a)

## Slide 29: 9.1.1. The CS Amplifier
Determining Vo/Vsig
  figure 9.2(b) illustrates this process
  circuit with dc sources eliminated
  small-signal analysis
  ignore ro
Figure 9.2: (b) Analysis of the CS amplifier to determine its low-frequency transfer function. For simplicity, ro is neglected.
(a)
(b)

## Slide 30: 9.1.1. The CS Amplifier
The effect of the coupling capacitor CC1 is to introduce a high-pass STC response with a break frequency P1.
(Since )
T-model of MosFet
1/gm
Notes: single-time-constant (STC)

## Slide 31: 9.1.1. The CS Amplifier
CC2 introduces a third STC high-pass factor,
(All capacitors are short-circuited. Use π-model)

## Slide 32
Determining the lower 3-dB frequency
  * Coupling and by-pass capacitors result in a high-pass frequency response with three poles
  * If the poles are sufficiently separated
    Bode plot can be used to evaluate the response for simplicity
    The lower 3-dB frequency is the highest-frequency pole
    P2 is typically the highest-frequency pole due to small resistance of 1/gm
  * If the poles are located closely
    The lower 3-dB frequency has to be evaluated by the transfer function which is more complicated
Determining the pole frequency by inspection
  * Reduce Vsig to zero
  * Consider each capacitor separately (treat the other capacitors as short
  circuit)
  * Find the total resistance between the terminals of each capacitor.
Selecting values for the coupling and by-pass capacitors
  * These capacitors are typically required for discrete amplifier designs
  * CS is first determined to satisfy needed fL
  * CC1 and CC2 are chosen such that poles are 5 to 10 times lower than fL
9.1.1. The CS Amplifier

## Slide 33
Figure 9.3: Sketch of the low-frequency magnitude response of a CS amplifier for which the three pole frequencies are sufficiently separated for their effects to appear distinct.

## Slide 34: 9.1.1. The CS Amplifier - Example 9.1
We wish to select appropriate values for the coupling capacitors CC1 and CC2 and the bypass capacitor CS for a CS amplifier for which RG = 4.7 MΩ, RD = RL = 15 kΩ, Rsig = 100 kΩ, and gm = 1 mA/V.
It is required to have fL at 100 Hz and that the nearest break frequency be at least a decade lower.

## Slide 35
9.1.1. The CS Amplifier - Example 9.1
Solution

## Slide 36: 9.1.2. The CE Amplifier
Figure 9.4. shows common-emitter amplifier.
  coupling capacitors CC1 & CC2
  emitter bypass capacitor CE
Effect of these capacitors felt at low frequencies.
Objective is to determine amplifier gain and transfer function.
This analysis is somewhat more complicated than CS case.
(a)
(b)
The circuit prepared for small-signal
analysis
Low frequency small signal analysis:
1) Eliminate the DC source
2) Ignore Cπ and Cμ and ro
3) Ignore rx, which is much smaller than rπ

## Slide 37
Two capacitances Cπ and Cμ , where
One resistance rx . Accurate value is obtained from high frequency measurement.
The High-Frequency Hybrid- Model

## Slide 38
9.1.2. The CE Amplifier
• Considering the effect of each of the three capacitors separately.
The voltage V at the base of the transistor can be written as
The output voltage is obtained as:
The effect of CC1 is determined with CE & CC2 assumed to be acting as short circuits:
Figure 9.5 (a)
Notes: consider the effect of the three capacitors CC1, CE, & CC2 one at a time.  when finding the effect of CC1, we shall assume that CE & CC2 are acting as perfect short circuits, and so on.

## Slide 39
9.1.2. The CE Amplifier

## Slide 40
9.1.2. The CE Amplifier
The effect of CE. For this purpose we assume that CC1 and CC2 are acting as perfect short circuits and thus obtain the circuit in Fig. 9.5(b)
Figure 9.5 (b)
Base current

## Slide 41
output voltage
9.1.2. The CE Amplifier
Thus the voltage gain including the effect of CE can be expressed

## Slide 42
9.1.2. The CE Amplifier
Finally, we consider the effect of CC2. The circuit with CC1 and CE assumed to be acting as perfect short circuits is shown in Fig. 9.5(c), for which we can write
low-frequency gain including the effect
of CC2
Figure 9.5: (c)

## Slide 43
9.1.2. The CE Amplifier
We observe that CC2 introduces the frequency-dependent factor between the square brackets, which we recognize as the transfer function of a high-pass STC circuit with a pole frequency ωP3,
(RC + RL) is the resistance seen between the terminals of CC2 when Vsig is set to zero.  CC2 causes the low-frequency gain of the amplifier to decrease at the rate of 6 dB/octave with a 3-dB frequency at as illustrated by the sketch in Fig. 9.5(c).
Figure 9.5: (c)

## Slide 44
where RC1, RE, and RC2 are the resistances seen by CC1, CE, and CC2, respectively, when Vsig is set to zero and the other two capacitances are replaced with short circuits.
9.1.2. The CE Amplifier

## Slide 45: Selecting Values for CC1, CE, and CC2
Selecting Values for CC1, CE, and CC2: We now address the design issue of selecting appropriate values for CC1, CE, and CC2. The design objective is to place the lower 3-dB frequency fL at a specified location while minimizing the capacitor values. Since, as mentioned above, CE usually sees the lowest of the three resistances, the total capacitance is minimized by selecting CE so that its contribution to fL is dominant. That is, by reference to Eq. (9.18), we may select CE such that is, say, 80% of ωL = 2π fL, leaving each of the other capacitors to contribute 10% to the value of ωL.