## Slide 1
Quiz 4.1
Deadline: April 10, 2020
a) Fig. 1 shows the Mosfet circuit with RD = RL = 10 kΩ, Rsig = 50 kΩ, CC1 = 2.7nF and gm = 1 mA/V.
Find Cs to obtain cutoff frequency fL = 200Hz.
If the break frequencies due to CC1 and CC2 are (the same) 20Hz, find RG and CC2.
Find the voltage gain vo/vsig when all capacitors are considered as short-circuit.
Fig. 1
Fig. 2
b) Fig. 2 shows the BJT circuit with RC = RL = 5 kΩ, Rsig = 2 kΩ, CE = 22μF, RB = 82kΩ, Ic = 1mA and β = 100.
If we select CE such that is, say, 80% of ωL = 2πfL, Find fL.
If each of the other capacitors to contribute 10% to the value of ωL, find CC1 and CC2.
Find the voltage gain vo/vsig when all capacitors are considered as short-circuit.