## Slide 1
Text book:
Sedra and Smith, “Microelectronic Circuits,” 6th Edition.
Souce: Blackboard to download materials
Lecture # 5: Feedback
International University
School of Electrical Engineering
ANALOG ELECTRONICS

## Slide 2: Introduction
IN THIS CHAPTER YOU WILL LEARN
  The general structure of the negative-feedback amplifier and the basic principle that underlies its operation.
  The advantages of negative feedback, how these come about, and at what cost.
  The appropriate feedback topology to employ with each of the four amplifier types: voltage, current, trans-conductance, and trans-resistance.
  Why and how negative-feedback amplifiers may be unstable (i.e. oscillate) and how to design the circuit to ensure stable performance.

## Slide 3: Introduction
Most physical systems incorporate some sort of feedback.
Feedback can be negative (degenerative) or positive (regenerative).
Feedback may be used to:
  desensitize the gain
  reduce nonlinear distortion
  reduce the effect of noise
  control the input and output resistances
  extend bandwidth
These characteristics result, however, in loss of gain.
  “The basic idea of negative feedback is to trade-off gain for other desirable properties.”
Notes: Most physical systems incorporate some form of feedback. It is interesting to note, though,
that the theory of negative feedback has been developed by electronics engineers. In his
search for methods for the design of amplifiers with stable gain for use in telephone
repeaters, Harold Black, an electronics engineer with the Western Electric Company,
invented the feedback amplifier in 1928. Since then the technique has been so widely used
that it is almost impossible to think of electronic circuits without some form of feedback,
either implicit or explicit.

## Slide 4: Introduction
Under certain conditions, negative feedback can be come positive.
  This causes oscillation.
However, positive feedback does not always lead to instability.
  Regenerative feedback has a number of applications – specifically, in active filtering.
No input
output
Oscillation circuit

## Slide 5: 10.1. The General Feedback Structure
Figure 10.1. shows the basic structure of a feedback amplifier – signal-flow diagram.
Open-loop amplifier has gain A (xo = Axi).
Figure 10.1: General structure of the feedback amplifier. This is a signal-flow diagram, and the quantities x represent either voltage or current signals.
In electronic circuits, part of or all output signal is fed back to input, and affects the input signal value, which is called feedback.

## Slide 6: 10.1. The General Feedback Structure
 Open-loop gain: A
 Feedback factor:   xf = xo
 Loop gain: A
 Amount of feedback: 1 + A
 Gain of the feedback amplifier (closed-loop gain):
Negative feedback:
 The feedback signal xf is subtracted from the source signal xs
 Negative feedback reduces the signal that appears at the input of the basic
amplifier
 The gain of the feedback amplifier Af is smaller than open-loop gain A by a factor of (1+A)
The loop gain A is typically large (A >>1):
 The gain of the feedback amplifier (closed-loop gain) Af  1/ 
 The closed-loop gain is almost entirely determined by the feedback network
 better accuracy of Af
  error signal xi = xs – xf
xo = Axi = A(xs – xf)
xo = A(xs – βxo)
Af = xo/xs = A/(1+Aβ)

## Slide 7
Negative feedback and positive feedback according to the effecting of feedback
1) positive feedback increases the signal that appears at the input of the basic amplifier
2) negative feedback reduces the signal that appears at the input of the basic amplifier
DC feedback and AC feedback
Feedback quantity only contains DC quantity is called DC
feedback
2) Feedback quantity only contains AC quantity is called AC
feedback
Usually AC feedback and DC feedback are concomitant

## Slide 8: Example 10.1
The feedback amplifier is based on an opamp with infinite input resistance and zero output resistance
(a) Find an expression for the feedback factor.
(b) Find the condition under which the closed-loop gain Af is almost entirely determined by the feedback network.
(c) If the open-loop gain A = 10000 V/V, find R2/R1 to obtain a closed-loop gain Af of 10 V/V.
(d) What is the amount of feedback in decibel?
(e) If Vs = 1 V, find Vo, Vf and Vi.
(f) If A decreases by 20%, what is the corresponding decrease in Af?
Fig. 10.2 (a) A non-inverting op-amp circuit for Example 10.1.

## Slide 9: Solution
Fig. 10. 2 (b) The circuit in (a) with the op-amp replaced with its equivalent circuit.
(a) Fig. 10.2(a) has the equivalent-circuit model, as shown in Fig. 10.2(b). The op amp is simply an ideal voltage-controlled voltage source of gain A. From Fig. 10.2(b) : the feedback network, consisting of the voltage divider (R1, R2), is connected directly to the output and feeds a signal Vf to the inverting input terminal of the op amp.  the zero output resistance of the op amp causes the output voltage to be AVi irrespective of the values of R1 & R2 and of RL. Thus, the feedback network and the load are assumed not to load the basic amplifier. Now we can easily determine the feedback factor β from
How is Vf subtracted from Vs at the input side?
+ No current flows in Rs  value of Rs doesn’t effect on Vi or the source “does not load” the amplifier input.
+ Vf will depend only on the ratio R1/R2 and not on the absolute values of R1 & R2
Vf

## Slide 10
Solution
(b) The closed-loop gain Af is given by Af = A / (1 + Aβ). We assume that Aβ >> 1
The condition can be stated as A >> Af
(c ) For A = 10000 V/V & Af = 10 V/V. It means that A >> Af. Thus we can select R1 & R2 to obtain β = 1/Af = 0.1 . Thus
R2 / R1 = 9 (approximation)
β = 0.0999 & R2/R1 = 9.01 (exact value)
(d) The amount of feedback is
which is 60 dB
(e) For Vs = 1 V  Vo = AfVs = 10  1 = 10 V and Vf = βVo = 0.0999  10 = 0.999 V
Vi = Vo / A = 10 / 104 = 0.001 V
(f) If A decreases by 20%, thus becoming A = 0.8 × 104 V/V
Af = 0.8 × 104 / (1 + 0.8  104  0.0999) = 9.9975 V/V
that is, it decreases by 0.025%, which is lower than the percentage change in A by approximately a factor (1 + Aβ)

## Slide 11: 10.2. Some Properties of Negative Feedback
10.2.1. Gain De-sensitivity dAf
  Equations (10.8) and (10.9) define de-sensitivity factor of (1+Ab).
The effect of negative feedback on desensitizing the closed-loop gain was demonstrated in Example 10.1, where we saw that a 20% reduction in the gain of the basic amplifier gave rise to only a 0.025% reduction in the gain of the closed-loop amplifier.
The percentage change in Af (due to variations in some circuit parameter) is smaller than the percentage change in A by the amount of feedback. For this reason the amount of feedback, 1 + Aβ, is also known as the de-sensitivity factor.
(10.8)
(10.9)

## Slide 12
10.2.2. Bandwidth Extension
  Equations (10.10) through (10.13) demonstrate how 3-dB frequencies may be shifted via negative feedback.
Consider an amplifier whose high-frequency response is characterized by a single pole. Its gain at mid and high frequencies can be expressed as
where AM denotes the midband gain and ωH is the upper 3-dB frequency.
Application of negative feedback, with a frequency-independent factor β, around this amplifier results in a closed-loop gain Af(s) given by
Thus the feedback amplifier will have a midband gain of AM/(1+AMβ) and an upper 3-dB frequency Hf = H(1+AMβ). (10.12)
Similarly, the open-loop gain is characterized by a dominant low frequency pole, then it has the feedback amplifier with a lower 3-dB frequency
Lf = L / (1 + AMβ) (10.13)
Note that the amplifier bandwidth is increased by the same factor by which its midband gain is decreased, maintaining the gain-bandwidth product at a constant value.
(10.10)
(10.11)
10.2. Some Properties of Negative Feedback

## Slide 13
Negative feedback:
Reduces the gain by a factor of (1+AMβ)
Extends the bandwidth by a factor of (1+AMβ)

## Slide 14
10.2.3. Interference Reduction
  Negative feedback can be employed to reduce the interference in an amplifier
  Signal-to-interference ratio (S/I = Vs/Vn) (10.14)
Figure 10.4 Illustrating the application of negative feedback to improve the signal-to-interference ratio in amplifiers.
interference,
10.2. Some Properties of Negative Feedback

## Slide 15
Figure 10.4: Illustrating the application of negative feedback to improve the signal-to-interference ratio in amplifiers.
Consider the circuit in Fig. 10.4(b). Here we assume that another amplifier stage with gain A2 that does not suffer from the interference problem.
The output voltage of the circuit in Fig. 10.4(b) can be found by superposition:
which is times higher than in the original case
10.2. Some Properties of Negative Feedback

## Slide 16
10.2.4. Reduction in Nonlinear Distortion
The amplifier transfer characteristic is linearized through the application of negative feedback
10.2. Some Properties of Negative Feedback

## Slide 17: 10.3. The Four Basic Feedback Topologies
Figure: 4 basic feedback topologies: (a) voltage-mixing voltage-sampling (series–shunt) topology; (b) current-mixing current-sampling (shunt–series) topology; (c) voltage-mixing current-sampling (series–series) topology; (d) current-mixing voltage-sampling (shunt–shunt) topology.

## Slide 18: 10.3.1. Voltage Amplifiers
voltage amplifiers – accept input voltage and yield output voltage.
  voltage-controlled voltage source (VCVS)
The feedback network should sample the output voltage. Also, because of the Thévenin representation of the source, the feedback signal xf should be a voltage that can be mixed with the source voltage in series.

## Slide 19: 10.3.1. Voltage Amplifiers
voltage-mixing / voltage-sampling – is the topology most suitable for voltage amps (Fig. 10.6).
  Is also known as series-shunt feedback.
  Input resistance  due to series connection
  Output resistance ↓ due to shunt connection
Figure 10.6: Block diagram of a feedback voltage amplifier. Here the appropriate feedback topology is series–shunt.

## Slide 20
Increased input resistance results because Vf subtracts from Vs, resulting in smaller signal Vi at the input.
  Low Vi causes input current to be smaller.
  This effects higher input resistance.
Decrease output resistance results because feedback works to keep Vo as constant as possible.
  DVo and DIo change / vary together.
  This effects lower output resistance.
10.3.1. Voltage Amplifiers

## Slide 21
Figure 10.7: Examples of a feedback voltage amplifier. All these circuits employ series–shunt feedback. Note that the dc bias circuits are only partially shown.
(c)
Noninverting op-amp. The feedback network:
R1, R2, develops a voltage that is applied to the
negative input terminal of the op amp.
As Vs , Vo  and Vf . Thus the change in Vf is of the same polarity as the change in Vs and the feedback is negative.
2 FET amplifier stages in cascade. Vo is sampled by the feedback network composed of the voltage divider (R1, R2), and the feedback signal is fed to the source terminal of Q1.
Vs , drain voltage of Q1 , voltage gate of Q2 ,  drain voltage of Q2
The feedback network will then cause Vs to , which is the same change in polarity initially assumed for Vs. Thus the feedback is indeed negative
CG transistor Q. Subtraction of Vf from Vs is effected by applying Vs to the source,  input Vi = Vs – Vf.
If Vs   Vd (which is Vo)  & Vf   Vf & Vs change in the same direction, verifying
that the feedback is negative.
Series-Shunt Examples

## Slide 22: 10.3.2. Current Amplifiers
current amplifier – accepts input current to generate output current.
  CCCS
  Norton Source
current-mixing / current-sampling – topology is most suitable for current amps.
  Is also known as shunt-series feedback.
  It not only stabilizes the current gain but also provides low input resistance/high output resistance.
Block diagram of a feedback current amplifier. Here, the appropriate feedback topology is the shunt–series.
Feedback network should sample the output current.
Feedback signal should be in current form so that it may be
mixed in shunt with the source current.
Notes:   CCCS = current control current source

## Slide 23
Figure 10.8: Example of a feedback current amplifier.
a CG stage Q1 followed by a CS stage Q2.
A sample of Io is obtained by placing a small resistance RM in series with RL.
The voltage developed across RM is fed via a large resistance RF to the source node of Q1. The feedback current If that flows through RF is subtracted from Is at the source node, resulting in the input current Ii = Is - If.
Is  causes Ii to increase and the drain voltage of Q1 will    the gate voltage of the p-channel device Q2, Io drain current of Q2 ↓  the voltage across RM will ↓,  If .
10.3.2. Current Amplifiers

## Slide 24: 10.3.3. Transconductance Amplifiers
transconductance amplifier – accepts input voltage and generates output current.
  VCCS
  Norton Source Output
voltage-mixing / current-sampling – topology is most suitable for transconductance amps.
  Is also known as series-series feedback.
Figure 10.10: (a) Block diagram of a feedback transconductance amplifier. Here, the appropriate feedback topology is series–series.
The sampling of the output current results in an increased output resistance. series–series feedback topology provides the transconductance amplifier with the desirable properties of increased input and output resistances.

## Slide 25
Figure 10.10: (b) Example of a feedback transconductance amplifier. (c) Another example.
A differential amplifier A1 followed by a CS stage Q2.
 Vs will result in a negative change at the gate of Q2   Io.   Vf , which is the
same polarity assumed for the change in Vs  the feedback is negative.
A CS amplifier Q1 in cascade with another CS amplifier Q2.

## Slide 26: 10.3.4. Transresistance Amplifiers
transresistance amplifier – accepts input current and generates output voltage.
  CCVS
  Thevenin Source Output
current-mixing / voltage-sampling – topology is most suitable for current amps.
  Is also known as shunt-shunt feedback.
  Provides low input resistance/low output resistance.
Figure 10.11: (a) Block diagram of a feedback transresistance amplifier. Here, the appropriate feedback topology is shunt–shunt.

## Slide 27
Figure 10.11: (b), (c), and (d) Examples of feedback transresistance amplifiers.
Examples of feedback transresistance amplifiers
An op amp with a feedback resistance RF that senses Vo and provides a feedback current If that is subtracted from Is at the input node.
A CG stage Q1 cascaded with a CS stage Q2. A feedback
resistor RF senses Vo and feeds a current if to the input node, where the subtraction
from Is takes place.
a CE stage Q1 cascaded with an emitter follower Q2. A feedback resistor RF senses Vo and feeds back a current If to the input node, where it is subtracted from Is.

## Slide 28: 10.4. The Feedback Voltage Amplifier (Series–Shunt)
Series-shunt is appropriate feedback for voltage amplifier. It consists of
  Unilateral open-loop amplifier (circuit A).
  Ideal Voltage-Sampling, voltage-mixing feedback network (b circuit)
  Input resistance Ri
  Open Circuit Gain A
  Output resistance Ro
Figure 10.12: The series–shunt feedback amplifier: (a) ideal structure
Note that the β circuit does not load the A circuit; that is, connecting the β circuit does not change the value of A
(A = Vo / Vi)

## Slide 29
Figure 10.12: (b) equivalent circuit of The series–shunt feedback amplifier
Af is the open-circuit voltage gain of the feedback amplifier, Rif is its input resistance, and Rof is its output resistance.

## Slide 30: The Ideal Case
The circuit of Fig. 10.12(a) has:

## Slide 31
Figure 10.13: Determining the output resistance of the feedback amplifier of Fig. 10.12(a): Rof = Vx /Ix.
Fig. 10.13 is used to determine the output resistance Rof of the feedback amplifier.
Set Vs = 0 and apply a test voltage Vx
Output resistance of the feedback amplifier

## Slide 32: 10.5. The Feedback Transresistance Amplifier (Shunt–Shunt)
Figure 10.24: (a) Ideal structure for the shunt–shunt feedback amplifier. (b) Equivalent circuit of the amplifier in (a).
Ideal case
Input resistance of the feedback amplifier
Output resistance of the feedback amplifier
Voltage gain of the feedback amplifier

## Slide 33: 10.6. The Feedback Current Amplifier (Shunt–Series)
Figure 10.28: (a) Ideal structure for the shunt–series feedback amplifier. (b) Equivalent circuit of the amplifier in (a).
Ideal case
Input resistance of the feedback amplifier
Output resistance of the feedback amplifier
Rof = (1 + Aβ )Ro
Voltage gain of the feedback amplifier

## Slide 34: 10.7. Summary of Feedback Analysis Method
Always begin analysis by determining an approximate value for the closed-loop gain (Af).
  Assume that loop gain Ab is large.
  Af = 1/b
  This value should serve for final check on Af.
The shunt connection at input or output will always result in reducing the corresponding resistance.
In utilizing negative feedback to improve the properties of an amplifier under design, the starting point is selection of feedback topology.
  Feedback factor (b.) may be determined as 1/Af.

## Slide 35: 10.8 The Stability Problem
In a feedback amplifier, the open loop gain (A) is generally a function of frequency.
Therefore, it should be called open-loop transfer function A(s).
One big question is: What happens to gain at higher frequencies?
  This has huge implications on stability of the amplifier.
10.8.1 Transfer Function of the Feedback Amplifier

## Slide 36: 10.8 The Stability Problem
10.8.1 Transfer Function of the Feedback Amplifier
|L|
|L|

## Slide 37: 10.8.2. Nyquist Plot
A plot used to evaluate the stability of a feedback amplifier
Plot the loop gain versus frequency on the complex plane
Stability:
  The plot does not encircle the point (-1, 0)

## Slide 38: 10.9. Effect of Feedback on the Amplifier Poles
Figure 10.35: Relationship between pole location and transient response.
The impulse response for a transfer
function with poles at σo±jωn will
contain the term:
The amplifier frequency response and stability are determined directly by its poles

## Slide 39: Poles of the Feedback Amplifier
 Called characteristic equation
The feedback amplifier poles are obtained by solving the characteristic equation
Amplifier with single-pole response
feedback moves the pole along the negative real axis

## Slide 40: 10.10. Effect of Feedback on the Amplifier Poles
Figure 10.36: Effect of feedback on (a) the pole location and (b) the frequency response of an amplifier having a single-pole, open-loop response.
The feedback amplifier is still a single-pole system
The pole moves away from origin in the s-plane as feedback (β) increases
The bandwidth is extended by feedback at the cost of a reduction in gain
Unconditionally stable system (the pole never enters the right-half plane)

## Slide 41: 10.11. Stability Study Using Bode Plots
Gain and phase margin
+ The stability of a feedback amplifier is determined by examining its loop gain as a function of frequency.
+ One of the simplest means is through the use of Bode plot for Aβ.
Stability is ensured if the magnitude of the loop gain is less than unity at a frequency shift of 180.
* Gain margin:
+ The difference between the value |Aβ| of at 180 and unity.
+ Gain margin represents the amount by which the loop gain can be increased while maintaining stability.
* Phase margin:
A feedback amplifier is stable if the phase is
less than 180 at a frequency for which |Aβ| =1.
A feedback amplifier is unstable if the phase is
in excess of 180 at a frequency for which |Aβ| =1.
The difference between the a frequency
for which |Aβ| =1 and 180.
Figure 10.42 Bode plot for the loop gain Aβ illustrating the definitions of the gain and phase margins

## Slide 42: Summary
Negative feedback is employed to make the amplifier gain less sensitive to component variations; to control input and output impedances; to extend bandwidth; to reduce nonlinear distortion; and to enhance signal-to-interference ratio.
The advantages above are obtained at the expense of a reduction in gain and at the risk of the amplifier becoming unstable (that is, oscillating). The latter problem is solved by careful design.
For each of the four basic types of amplifier, there is an appropriate feedback topology. The four topologies, together with their analysis procedures, are summarized in Table 10.1.

## Slide 43: Summary
The key feedback parameter are the loop gain (Ab.), which for negative feedback must be a positive dimensionless number, and the amount of feedback (1+Ab.). The latter directly determines gain reduction, gain desensitivity, bandwidth extension, and changes in input and output resistances.
Since A and b are in general frequency dependent, the poles of the feedback amplifier are obtained by solving the characteristic equation 1+A(s)b(s) = 0.
For the feedback amplifier to be stable, its poles must all be in the left-hand side of the s-plane.
Stability is guaranteed if at the frequency for which the phase angle of Ab is 180O, |Ab| is less than unity; the amount by which it is less than unity, expressed in decibels, is the gain margin. Alternatively, the amplifier is stable if, at the frequency at which |Ab| = 1, the phase angle is less than 180O, the difference ifs the phase margin.