## Slide 1
Question 1
The KHN biquad is depicted in Fig. 1 with C = 0.01μF, R2 = 1kΩ and R1 = 2kΩ.
Design (determine R, Rf and R3) a bandpass filter with center frequency and quality factor Q = 5. (Hint: ωo = 1/RC)
Give the numeric expression of the transfer function for the bandpass filter of Fig. 1.
Determine low and high cut-off frequencies of the filter.
Quiz 7.2
Deadline: June 12, 2020
Fig. 1
Question 2
The bandpass filer is depicted in Fig. 2 with C1 = 2.2nF, R3 = 20k Ω , R4 = 2kΩ and α = 0.5.
Determine C2 to obtain center frequency .
Determine bandwidth and quality factor of the filter.
Plot another version of this circuit.
Fig. 2