## Slide 1: Sinusoidal Steady-State Analysis
Textbook:
Electric Circuits
James W. Nilsson & Susan A. Riedel
9th Edition.
We consider circuits energized by time-varying voltage or current sources.

## Slide 2: Outline
Complex Numbers Tutorial
Sinusoids
Phasors
Techniques of Circuit Analysis
Phasor Diagrams

## Slide 3
The transformer
A transformer is a device that is based on magnetic coupling.
Are used in both communication and power circuits.
In communication circuits: transformer is used to matched impedance and eliminate dc signals from portions of the systems
In power circuits: transformer is used to establish ac voltage levels that facilitate the transmission, distribution and consumption of electrical power.

## Slide 4
Primarily used in communication circuits.
Is formed when two coils are wound on a single core to ensure magnetic coupling.
Frequency domain circuit model of a transformer
Linear transformer
Primary winding
Secondary winding
R1 = the resistance of the primary winding
R2 = the resistance of the secondary winding
L1 = the self-inductance of the primary winding
L2 = the self-inductance of the secondary winding
M = the mutual inductance
Vs = sinusoidal source
Zs = internal impedance of the source
ZL = the load
I1 = primary current
I2 = secondary current

## Slide 5
Transformer circuit analysis
Mesh-current equations:
Yield:

## Slide 6
Transformer circuit analysis
Impedance at the terminal of the source:
Zab is independent of the magnetic polarity of the transformer.
Zab shows how the transformer affects the impedance of the load as seen from the source

## Slide 7
Reflected impedance
Zr = reflected impedance
= the impedance of the secondary circuit as seen from
the terminals of the primary circuit or vice versa.
Notes:
The reflected impedance is due solely to the existence of mutual inductance
The linear transformer reflects the conjugate of the self-impedance of the secondary circuit (Z*22) into the primary winding by a scalar multiplier
Z*22

## Slide 8
Example
The parameters of a certain linear transformer are R1 = 200 , R2 = 100 , L1 = 9H, L2 = 4H, and k = 0.5. The transformer couples an impedance consisting of an 800  resistor in series with a 1 F capacitor to a sinusoidal voltage source. The 300 V (rms) source has an internal impedance of 500 + j100  and a frequency of 400 rad/s.
a) Construct a frequency-domain equivalent circuit of the system.
b) Calculate the self-impedance of the primary circuit.
c) Calculate the self-impedance of the secondary circuit.
d) Calculate the impedance reflected into the primary winding.
e) Calculate the scaling factor for the reflected impedance.
f) Calculate the impedance seen looking into the primary terminals of the transformer.
g) Calculate the Thevenin equivalent with respect to the terminals c, d.

## Slide 9
Example – Sol.
The figure shows the frequency-domain equivalent circuit. Note that the internal voltage of the source serves as the reference phasor, and that
V1 and V2 represent the terminal voltages of the transformer. In the circuit of the figure, we made the following calculations:

## Slide 10
Example – Sol.
b) The self-impedance of the primary circuit is
Z11 = 500 + j100 + 200 + j3600 = 700 + j3700 .
c) The self-impedance of the secondary circuit is
Z22 = 100 + j1600 + 800 - j2500 = 900 - j900 .
d) The impedance reflected into the primary winding is
e) The scaling factor by which Z*22 is reflected is 8/9.
f) The impedance seen looking into the primary terminals of the transformer is the impedance of the primary winding plus the reflected impedance; thus
Zab = 200 + j3600 + 800 + j800 = 1000 + j4400 .

## Slide 11
Example – Sol.
g) The Thevenin voltage will equal the open circuit value of Vcd. The open circuit value of Vcd will equal j1200 times the open circuit value of I1.
The open circuit value of I1 is
Therefore
The Thevenin impedance will be equal to the impedance of the secondary winding plus the impedance reflected from the primary when the voltage source is replaced by a short-circuit. Thus

## Slide 12
Example – Sol.
The Thevenin equivalent is shown in the figure bellow

## Slide 13
Usually used to model the ferromagnetic transformer in power systems.
An ideal transformer consists of two magnetically coupled coils having N1 and N2 turns, respectively, and exhibiting these three properties:
1) The coefficient of coupling is unity (k = 1)
2) The self-inductance of each coil is infinite (L1 = L2 = ∞)
3) The coil losses, due to parasitic resistance, are negligible (R1 = R2 = 0)
Ideal transformer

## Slide 14
Ideal transformer
The circuit behavior is governed by the turns ratio a = N2/N1
Volts per turns is the same for each winding
Ampere turns are the same for each winding
If the coil voltages V1 and V2 are both positive or negative at the dot-marked terminal, use a plus (+) sign. Otherwise, use a negative (-) sign.
If the coil current I1 and I2 are both directed into or out of the dot-marked terminal, use a minus (-) sign. Otherwise, use a plus (+) sign.

## Slide 16
V2
Ideal transformer
Turns ratio:
Three ways to show the turns ratio of an ideal transformer

## Slide 17
Impedance matching by using ideal transformer
Relation of V1 and I1 by the transformer turns ratio:
Impedance seen by the source and load respectively:
Yield:
The ideal transformer’s secondary coil reflects the load impedance back to the primary coil with the scaling factor 1/a2.